## Slide 1
Safe collection, transport and storage of samples from patients suspected to be infected with Ebola
Rapid Response Teams Training
Updated: May 2018

## Slide 2: Learning objectives
At the end of this session you should be able to:
* Follow the key steps of a safe blood sample collection;
* Pack the blood samples in order to transport them to the laboratory;
* Ensure appropriate storage of sample

## Slide 3: Outline
Introduction
Steps for Sample Collection
Sample transport
Key messages
References

## Slide 4
Improves lab efficiency
Directly
affects patient
care
Influences therapeutic
decisions
Essentiel for a correct
diagnosis
Good sample
management
1. Introduction

## Slide 5: Mismanagement of samples can produce…
Delays in reporting of results
Repetition of unnecessary tests
Increase in cost
Misdiagnosis, mistreatment
Injury
Death

## Slide 6: 2. Steps for Sample Collection
Get ready: label containers and forms and assemble all equipment and materials before approaching the patient
Protect yourself: put on complete personal protective equipment (PPE)
Collect sample: use sterile technique and safety precautions
Make it safe: prepare sample container for transport
Clean up: manage waste, spills and accidental exposures

## Slide 7: a) Get Ready
Introduce yourself to the patient and explain what you will do and why.
Record keeping is crucial;
  Collect epidemiological information about patient and fill out on the case investigation form (CIF) or standard national request form;
  Label the form and the primary container with a minimum of three identifiers: sample name or unique ID, date of collection, time of collection.
Ensure you have a helper nearby to
assist you with PPE and additional
equipment.

## Slide 8: b) Protect Yourself
WASH
YOUR HANDS BEFORE AND AFTER PATIENT CONTACT AND BETWEEN PATIENTS
THE MINIMUM RECOMMENDATION IS UNIVERSAL PPE. THIS INCLUDES GLOVES, GOWN AND EYE PROTECTION
WEAR FULL PPE: double gloves, gown, full respiratory protection, boots

## Slide 9: b) PPE Levels
UNIVERSAL PPE
FULL PPE
BLOOD BORNE
N-95 Mask
Double gloves
Face shield
Boots
Gloves
Gown
Eye protection (goggles)
G.Pellegrini, CDC
Notes: Notes for facilitators:
reflect with the audience on what to do if adequate PPE is not available

## Slide 10: c) Blood Samples
A person trained in phlebotomy should take the sample
Contact the laboratory to confirm the sample type, the volume needed, tube to be used, storage and transport temperature, etc.
For PCR, use a plastic EDTA tube to collect whole blood (avoid heparin tubes);
  CAUTION! Color of EDTA tube caps is not standardized.
Invert the tubes after collection for gentle mixing;
If a venous blood sample cannot be taken, a swab from finger prick may be collected in some instances.
For GeneXpert testing, follow the sample collection steps on the following slide.

## Slide 11: c) Post-Mortem Samples
The RRT may be responding to a death report:
If a person is suspected to have died from EVD, a buccal (oral fluid) swab can be taken

## Slide 12
Ebola suspect or probable case
Capillary blood
For local inactivation and testing by GeneXpert RT-PCR
For screening using an RDT where PCR is not readily available (e.g. investigation of remote outbreaks)
Venous blood
Whole blood in EDTA tube
Transport and storage at 2-8°C or for immediate local testing by GeneXpert
Oral swab
Transport and storage at 2-8°C for PCR
Local inactivation and GeneXpert PCR testing
Direct screening by RDT (e.g. Oraquick Ebola)
Blood collection is possible
No (cadaver)
Yes
/!\ Maximum precautions are required during collection, storage and transport of the sample
history of contact Symptoms: Illness with onset of fever and no response to treatment for usual causes of fever in the area, and at least one of the following signs: bloody diarrhoea, bleeding from gums, bleeding into skin (purpura), bleeding into eyes and urine preliminary lab results (malaria RDT +/- Ebola RDT) I’ve inserted a next slide with the definitions of a suspect case in DRC that you can use to edit the text above.
Notes: Note: differential diagnosis includes malaria

## Slide 13
Is PCR readily available?
Perform PCR
Is the PCR positive?
Is an RDT readily available?
YES
NO
Outbreak response triggered
Has it been >72 hours since onset of symptoms?
YES
NO
Redo the PCR >72 hours after onset
Not a case, no further response required
Perform RDT
Is the RDT reactive?
Refer patient to a facility where testing is possible
Send specimen for PCR confirmation, begin outbreak response and re-evaluate when PCR result available
Send specimen for PCR confirmation, await results or commence isolation, depending on estimated risk
YES
YES
YES
NO
NO
NO
Testing algorithm for live suspects
Choices may vary with stage of outbreak

## Slide 14: Testing choices
RT-PCR from EDTA whole blood is the reference method for confirmatory Ebola testing during acute illness.
Collected blood can be tested-on site if GeneXpert is available, or shipped to a reference lab.
If the sample is to be shipped, gravity-sediment and remove the plasma (in glove box) for triple packing & transport at ambient temp. (2-8°C if feasible).
RT-PCR using GeneXpert (Xpert Ebola assay) can be performed on inactivated whole blood, capillary blood or plasma. Sample can be inactivated by collector under PPE or afterward in a glove box. Sample in inactivation solution is stable for 24 hours at ambient temperature. See SOP.
RDT testing for Ebola antigens should be reserved for remote testing of Ebola suspect cases where PCR is not readily available. Both positive and negative results should be confirmed by PCR.
Elisa for IgM or IgG is reserved for retrospective testing in patients who have recovered and were not confirmed by PCR in the acute phase of illness.

## Slide 15: d) Make it Safe
Place all items that came into contact with the sample into the infectious waste bag for destruction or perform a complete surface disinfection on it when possible;
Wipe the sample container with a disinfectant before handing it to your gloved designated helper, who can put it in a second, leak proof container and start preparing it for transport;
Have the helper tightly close the second container, seal and disinfect the container surface;
If there are multiple patients;
  Change gloves between each patient – do not reuse gloves!
  Wash hands between each patient.
Notes: Notes for facilitators: if hypochlorite is used for disinfecting the sample container, keep it mind that it degrades plastic bags (in which the sample container(s) may be placed) and can interfere with some laboratory tests (e.g. PCR) if it gets in the sample.

## Slide 16: e) Disinfection and Waste Disposal – general recommendations
Ensure sharps are disposed in a suitable container to minimize the risk of injury
Disinfect materials at source as much as possible using appropriate disinfectant (e.g. 10% hypochlorite freshly prepared);
Add small amount of disinfection solution to sharps containers;
Double bag and sealed hazardous waste;
Take hazardous waste to location where it can be properly disinfected and disposed of;
The RRT should manage all waste they create to protect the community and environment.
Notes: Notes for facilitators: 10% hypochlorite is 10,000 ppm. Hypochlorite solution (bleach) has to be freshly prepared, unless the hypochlorite solution includes a stabilizer.

## Slide 17: e) Waste Disposal
Depending on what is available on site, infectious waste can be disposed of in the following ways:
Incineration
Containment & burial
Infectious waste should be disinfected before disposal:
Autoclave
Chemical disinfection
Notes: Notes for facilitators: Disposal and disinfection methods are effective if equipment (e.g. autoclave, incinerator) or reagents (e.g. hypochlorite) are properly maintained/prepared and used strictly in accordance with appropriate protocols.
Incineration, due to high temperatures in the burn pit, can also be an effective disinfection method if used correctly. However, incineration, particularly in an open pit, is a much less controlled environment than autoclave and requires longer heating times and higher temperatures to be effective in disinfecting. Also keep in mind that:
an open fire has the potential to disperse viable organisms in the air currents;
burning waste treated with chlorine could generate dioxins which are carcinogenic;
burning certain types of plastics can release harmful chemicals.
Autoclaving provides a more controlled environment but effectiveness can be compromised by overloading, obstructing the circulation of steam, bags sealed too tightly, trying to autoclave sealed containers, etc.

## Slide 18: e) Spills and accidental exposure
Response to a spill of blood or bodily fluids:
  Move away from the spill area;
  Alert others in the area of the spill;
  Treat any potential exposures;
    Disinfect clothing splashes;
    Remove contaminated PPE;
    Seek medical attention for those exposed.
  Contain the spill;
    Cover with absorbent materials;
    Disinfect with an appropriate disinfectant, such as 10% hypochlorite freshly prepared;
    Remove sharps.
  Collect the waste;
    Gather the waste for proper disposal.
  Report the incident.

## Slide 19: 3. Sample transport How to Transport Samples
Different samples require different transportation and storage requirements based on the viability of the samples.
  Whole Blood: Transport from 2 to 8°C
Storage prior to transport: refrigerate 2 to 8°C (if not possible: 24h max at room temperature).
Do not freeze whole blood.
  Swabs: Transport and storage temperature for PCR testing, 2-8 degree target. For RDTs, follow the instructions on the instructions for use of each product.
CHECK WITH THE LABORATORY TO DETERMINE SAMPLE TRANSPORT REQUIREMENTS!

## Slide 20: National Sample Transport Systems
Many countries utilize modified sample transport systems to meet their daily needs.
Shipping containers can be disinfected and are reusable.
The Golden Rule for any sample transport is: Triple Packaging for protecting the worker, the sample and the environment
      Primary Package – is the sample container which is often placed within a sealable bag or a plastic container, with enough absorbent material to contain a spill.
      Secondary Package – is a sturdy waterproof sealable container used to protect the samples during transport and can contain multiple primary packages.
      Tertiary Package – can contain multiple secondary packages. It functions to regulate sample temperature, hold required documentation and protect the environment.
Notes: Notes to facilitators:
Primary package can be placed in sealable bag or plastic container to limit contamination of the workers from the outer surface of the primary package.
Primary container must be correctly marked with a minimum of three identifiers: sample name or unique ID, date of collection, time of collection.
Tertiary package must be correctly marked and labelled

## Slide 21: Documentation Laboratory and Epidemiological Forms
If no refrigeration is required, place the laboratory form/letter and epidemiological questionnaire inside the tertiary container.
If refrigeration is needed, place the documentation in a sealed envelope and attach to the outside of the tertiary container.
Protect the documents from moisture and public viewing.
RRT lab module

## Slide 22: 4. Key messages (1)
Sample collection and time between collection and processing directly affect the quality and reliability of the laboratory results.
Rapid delivery of the sample to the laboratory is important.
Make sure the carrier and laboratory can contact you if a problem arises or if they have questions concerning the sample shipment
Notify the laboratory in advance of the number of samples and their expected delivery time
Check with the carrier to ensure there are no issues with the shipment (e.g. customs)

## Slide 23: Key messages (2)
Consider the following;
  The types and number of samples required and the proper labeling of sample containers;
  If samples cannot be transported or tested immediately, they should be stored appropriately;
  It is your responsibility to remove hazardous waste and make it safe;
  If in any doubt, discuss your plans with the laboratory;
  Record all steps and keep the laboratory informed.

## Slide 24: 5. References
UN Recommendations on the Transport of Dangerous Goods, 2017 (http://www.unece.org/trans/danger/publi/unrec/rev20/20files_e.html)
ICAO Technical Instructions (https://www.icao.int/safety/DangerousGoods/Pages/technical-instructions.aspx)
IATA Packing Instruction 650 – Biological Substances, Category B (https://www.iata.org/whatwedo/cargo/dgr/Documents/packing-instruction-650-DGR56-en.pdf)
Specimen labeling, storage & handling, CDC, (https://www.cdc.gov/urdo/downloads/specstoragehandling.pdf)
WHO Guidance on regulations for the transport of infectious substances 2017–2018 (http://www.who.int/ihr/publications/WHO-WHE-CPI-2017.8/en/)
WHO Infectious Substances Shipping Training - a course for shippers (http://www.who.int/ihr/i_s_shipping_training/en/)
European Agreement on the International Carriage of Dangerous Goods by Road (ADR), 2017 (www.unece.org/trans/danger/publi/adr/adr2017/17contentse0.html)
Regulations on the International Carriage of Dangerous Goods by Rail (RID), 2017 (http://otif.org/en/?page_id=174)
Guideline for Disinfection and Sterilization in Healthcare Facilities, 2008, CDC
https://stacks.cdc.gov/view/cdc/11560
Guidelines for the collection of clinical specimens during field investigation of outbreaks, WHO/CDS/CSR/EDC/2000.4
http://www.who.int/ihr/publications/WHO_CDS_CSR_EDC_2000_4/en/
CDC Infectious Diseases Laboratories Test Directory, https://www.cdc.gov/laboratory/specimen-submission/list.html
Ebola outbreak, laboratory technical guidances, 2014 (http://www.who.int/csr/resources/publications/ebola/surveillance/en/index2.html)

## Slide 25: Disclaimer
WHO Health Security Learning Platform - Training Materials
These WHO Training Materials are © World Health Organization (WHO) 2018. All rights reserved.
Your use of these materials is subject to the “WHO Health Security Learning Platform, Training Materials – Terms of Use”, which you accepted when downloading them and which are available on the Health Security Learning Platform at: https://extranet.who.int/hslp .
Should you adapt, modify, translate, or in any other way revise the contents of these materials, you shall not imply that WHO is any way affiliated with such modifications and shall not use the WHO name or emblem in such modified materials.
Further, please inform WHO of any modifications of these materials that you use publicly, for record-keeping purposes and continued development, by emailing ihrhrt@who.int.

## Slide 26: Optional slides

## Slide 27: Zoom on Rapid Diagnostic Tests (RDTs)
The term RDT (rapid diagnostic tests) conventionally refers to lateral flow immunoassays like those used for malria.
For Ebola, their use is confined to screening in remote settings (for the time being) and the results (positive or negative) must be confirmed with molecular tests.
New RDTs are being developed all the time and new devices may be introduced during response situations
3c) Zoom on Rapid Diagnostic Tests (RDTs)
http://www.who.int/malaria/areas/diagnosis/rapid-diagnostic-tests/about-rdt/en/

## Slide 28: Triple Packaging
  Primary receptacle
  Watertight, leak-proof receptacle containing the sample.
  Package with enough absorbent material to absorb all fluid in case of breakage or leakage and to stabilize samples during transport.
  Secondary packaging
  Durable, watertight, leak-proof packaging to enclose and protect the primary receptacles.
  Several cushioned primary receptacles may be placed in one secondary packaging.
  Tertiary packaging
  Secondary packaging is placed in outer packaging with suitable cushioning material.
  May contains ice or dry ice (if necessary) to maintain sample temperature.
  Contains documentation.
Internationally, only packaging tested & approved using Packing Instruction 620 should be used for Cat A shipments. These packages are marked with a UN packaging symbol.
Packing Instruction 650 may be used to guide packaging of Cat B substances.
4G/CLASS 6.2/02
F/BVT 312103
u
n
ISST Training Programme
Notes: Notes to facilitators: Don’t enclose dry ice in airtight containers! Using dry ice is not common for outbreak investigation in the field.

## Slide 29: International Sample Transport Marks
UN 3373
INFECTIOUS SUBSTANCE,
AFFECTING HUMANS
UN 2814
BIOLOGICAL SUBSTANCE,
CATEGORY B
ISST Training Programme
Proper Shipping Name (PSN) of Infectious Substance
UN Number of Infectious Substance.
Name & Address of Shipper & Receiver
Emergency Name & Telephone Number of a Responsible Person (may be written on the airway bill for Cat B packages)
dry ice as coolant
UN1845
Net quantity ____kg
Indicators of dry ice (if applicable) including PSN, UN number and net quantity used
RRT lab module
RRT lab module
Notes: Notes for facilitators: «marks» are what need to be written on the shipping box: address, etc.

## Slide 30: International Sample Transport Labels
RRT lab module
RRT lab module
RRT lab module
For Cat A Substances:
Infectious Substances Label
For Packages containing more than 50mL substance:
Orientation arrows on opposite sides of the box
Cargo Aircraft Only (for shipments by air)
If Dry Ice is included:
Class 9. Miscellaneous Substances Label
Notes: Notes for facilitators: «labels» are internationally recognized and pre-defined symbols. They cannot be modified.