## Slide 1: External Quality Assessment
Assessment: EQA - Module 10
<number>
EQA - Module 12
<number>
External Quality Assessment
Notes: <number>

## Slide 2: Learning Objectives
Assessment: EQA - Module 10
<number>
<number>
<number>
At the end of this module, participants will be able to:
  Discuss the importance of an EQA program in improving the quality of laboratory test results.
  Describe at least three EQA methods and the advantages and disadvantages of each.
  Outline a method to investigate an unacceptable test result from an EQA sample.
Notes: <number>

## Slide 3: Scenario
Assessment: EQA - Module 10
<number>
<number>
<number>
A newly appointed laboratory supervisor has begun reviewing past EQA results, and observes poor Gram stain performance.
  “How should the laboratory investigate this problem?”
Notes: <number>

## Slide 4: The Quality Management System
Assessment: EQA - Module 10
<number>
<number>
Organization
Personnel
Equipment
Purchasing & Inventory
Process Control
Information Management
Documents & Records
Occurrence Management
Assessment
Process Improvement
Customer Service
Facilities & Safety

## Slide 5
Assessment: EQA - Module 10
<number>
External Quality Assessment
A system for objectively checking the laboratory’s performance using an
external agency or facility

## Slide 6
Assessment: EQA - Module 10
<number>
<number>
EQA Methods
Proficiency Testing
Rechecking Retesting
On-site Evaluation

## Slide 7: External Quality Assessment (EQA)
Assessment: EQA - Module 10
<number>
<number>
comparison among different test sites
early warning for systemic problems
objective evidence of testing quality
areas that need improvement
training needs

## Slide 8: EQA Benefits
Assessment: EQA - Module 10
<number>
Laboratory
oriented
objectives
Public Health oriented objectives

## Slide 9
Assessment: EQA - Module 10
<number>
<number>
Recognition /
Education
Mono / multi
Regional/
National/
International
Obligatory /
voluntary
Free / not free
Confidential
EQA

## Slide 10: EQA
Assessment: EQA - Module 10
<number>
important for improvement
a measure of laboratory performance

## Slide 11
Assessment: EQA - Module 10
<number>
<number>
ISO/IEC Guide 43-1:1997
“Proficiency testing schemes (PTS) are interlaboratory comparisons that are organized regularly to assess the performance of analytical laboratories and the competence of the analytical personnel.”
Definition Proficiency Testing

## Slide 12
Assessment: EQA - Module 10
<number>
<number>
CLSI GP27-A2 27:8
“A program in which multiple samples are periodically sent to members of a group of laboratories for analysis and/or identification; whereby each laboratory’s results are compared with those of other laboratories in the group and/or with an assigned value, and reported to the participating laboratories and others.”
Definition Proficiency Testing

## Slide 13
Assessment: EQA - Module 10
<number>
PT organization /provider
Laboratory
Analyze
Evaluation
PT performance report
Return results
PT Process
PT samples sent regularly
Receive PT report
Corrective Actions

## Slide 14
Assessment: EQA - Module 10
<number>
<number>
Laboratory 1
Laboratory 2
No discussion between labs
PT: Roles of Laboratory
Final PT report received
ISO 15189
Analyze same manner with same personnel
Improvement
PT sample
Patient sample

## Slide 15
Assessment: EQA - Module 10
<number>
Information received from PT participation must be directed toward improvement in the laboratory to receive the full value.
PT Results

## Slide 16
Assessment: EQA - Module 10
<number>
PT results are affected by variables not related to patient samples
PT will not detect all problems in the laboratory
PT may not detect problems with pre- and postexamination procedures
PT Limitations

## Slide 17: Other EQA Methods Rechecking/Retesting
Assessment: EQA - Module 10
<number>
Reference laboratory
Peripheral laboratory
Rechecking

## Slide 18: Retesting
Assessment: EQA - Module 10
<number>
<number>
tested by reference laboratory
performed on dried blood spots or serum
not blinded
statistically significant
primarily used to assess HIV rapid testing

## Slide 19: Rechecking
Assessment: EQA - Module 10
<number>
<number>
samples must be collected randomly
avoid systematic sampling bias
statistically significant
resolve discrepancies
effective feedback
primarily AFB

## Slide 20: Comparison of rechecking non-blinded and random blinded smears for acid-fast bacilli
Assessment: EQA - Module 10
<number>
<number>
Performance characteristics measured | Non-blinded sample (1998) | Random blinded sample (2002)
State A-sensitivity | 99.7% | 86.7%
State B-sensitivity | 98.9% | 84.7%
State A-specificity | 99.8% | 99.1%
State B-specificity | 99.9% | 99.7%
Martinez A, et al. Int J Tuberc Lung Dis 2005;9(3):301-5.

## Slide 21: On-site Evaluation
Assessment: EQA - Module 10
<number>
Laboratory
  to obtain a realistic picture of laboratory practices
  to provide assistance with problem areas
External group or Organizer
Periodic visits

## Slide 22: AFB Microscopy Comparison of performance before and after on-site monitoring
Assessment: EQA - Module 10
<number>
No sand bucket | 96 | 27
No decontamination of sputum cups | 60 | 23
No disinfectant | 31 | 4
No biohazard waste bin (covered) | 48 | 8
No lab coats | 48 | 46
Technologists do not wash hands | 17 | 4
Shortage of lab reagents | 75 | 27
Improper sputum collection | 60 | 31
Improper filling of laboratory register | 29 | 4
Improper labeling slides/containers | 31 | 13
Aziz, M. and G. Bretzel, Int J Tuberc Lung Dis 2002:6(4):340-349.
BEFORE (%)
AFTER(%)

## Slide 23: Proficiency Testing and Rechecking
Assessment: EQA - Module 10
<number>
<number>
Characteristics | PT | RC
Interlaboratory comparison | Yes | Yes
Simulated samples | Yes | No
Real samples | Yes/No | Yes
Time and resources needed | Less | More
Analytes evaluated | Many | Few

## Slide 24: EQA Participation
Assessment: EQA - Module 10
<number>
<number>
Recommended for all laboratories
Required by ISO
ISO 15189

## Slide 25: Management Process
Assessment: EQA - Module 10
<number>
handle and analyze EQA samples
treat EQA samples same as patient
monitor and maintain records
investigate deficiencies
manage corrective action efforts
communicate outcomes
EQA results
Corrective actions

## Slide 26: EQA performance problems
Assessment: EQA - Module 10
<number>
<number>
CHALLENGE
Sample Management
Examination
Report
Preexamination
Postexamination
PT PROVIDER

## Slide 27: EQA Should Lead to Actions
Assessment: EQA - Module 10
<number>
<number>
EQA
Identify
problems
Take Corrective
Action

## Slide 28: Summary
Assessment: EQA - Module 10
<number>
<number>
EQA is a system for objectively checking the laboratory’s performance using an external agency or facility
All laboratories should participate in EQA
Several methods of EQA in use
EQA samples must be treated the same as patient samples

## Slide 29: Key Messages
Assessment: EQA - Module 10
<number>
<number>
EQA uses valuable resources, make best possible use
EQA should not be punitive
EQA should be viewed as educational
EQA can help direct improvement efforts
EQA is a critical element of a quality management system

## Slide 30: Comments? Questions?
Assessment: EQA - Module 10
<number>
<number>
Organization
Personnel
Equipment
Purchasing & Inventory
Process Control
Information Management
Documents & Records
Occurrence Management
Assessment
Process Improvement
Customer Service
Facilities & Safety