## Slide 1: How to make 0.5% and 0.05% chlorine solution
B6.3b IPC
Speaker name

## Slide 2
This learning resource is part of the Rapid Response Team Advanced Training Package (RRT ATP) especially geared to RRT members.
Based on an all-hazard approach, the programme aims to provide RRT members with the advanced knowledge, skills, attitudes (KSA) and tools needed to early detect and effectively respond to a public health event.
The RRT ATP is a component of the Rapid Response Teams Training Programme.
Introduction

## Slide 3
At the end of this session, you should be able to:
Understand when chlorine is used
Understand when mild chlorine is used and when strong chlorine is used
Be familiar with the process of mixing chlorine of various strengths
Learning objectives
Notes: Print PDFs in appropriate language from this website: https://www.cdc.gov/vhf/ebola/hcp/mixing-chlorine-solutions.html

## Slide 4
Strong (0.5%) solution includes a higher concentration of HTH* (High Test Hypochlorite) chlorine can be used for disinfecting floors and surfaces, medical equipment, bedding, and gloved hands.
Cleaning and disinfection of environmental surfaces in the context of COVID-19
https://www.who.int/emergencies/diseases/novel-coronavirus-2019/technical-guidance-publications?healthtopics=b6bd35a3-cf4f-4851-8e80-85cb0068335b&publishingoffices=aeebab07-3d0c-4a24-b6ef-7c11b7139e43&healthtopics-hidden=true&publishingoffices-hidden=true
Mild (0.05%) solution is a gentler solution of HTH* chlorine can be used for washing bare hands in settings where other methods, such as soap and running water or alcohol-based hand rubs, are not available or cannot be used.
Use of 0.5% and 0.05% chlorine solution

## Slide 5: What you need to know
Wait 30 minutes before using any chlorine solution that is made from powder
Proper storage is important. Chlorine solutions, depending on their use, should to be transferred into bottles that have sprayers or dispensers that have spigots
Chlorine solutions need to be labeled with their correct strength. Label strong with (0.5%) and mild as (0.05%)

## Slide 6: What you need to know
Chlorine solutions do not work as well on heavily soiled surfaces. Clean first then disinfect
Keep the chlorine solution away from direct sunlight
Chlorine solutions lose strength over time, so make a fresh batch every day

## Slide 7
Source: https://www.cdc.gov/vhf/ebola/pdf/cleaning-hand-washing-with-chlorine-powder.pdf

## Slide 8
Source: http://www.cdc.gov/vhf/ebola/pdf/chlorine-solution-liquid-mild.pdf

## Slide 10
WHO Health Security Learning Platform - Training Materials
These WHO Training Materials are © World Health Organization (WHO) 2022. All rights reserved.
Your use of these materials is subject to the “WHO Health Security Learning Platform, Training Materials – Terms of Use”, which you accepted when downloading them and which are available on the Health Security Learning Platform at: https://extranet.who.int/hslp
Should you adapt, modify, translate, or in any other way revise the contents of these materials, you shall not imply that WHO is any way affiliated with such modifications and shall not use the WHO name or emblem in such modified materials.
Should you adapt, modify, translate, or in any other way revise the contents of these materials, you shall acknowledge the source of the material providing the following attribution: “These training materials are a modified version of the Rapid Response Teams Advanced Training Package (available at: https://extranet.who.int/hslp/), which is © the World Health Organization (WHO), 2022, and used with permission from WHO. WHO disclaims any responsibility for any modifications to, or revisions of, the WHO copyrighted materials.”
Further, please inform WHO of any modifications of these materials that you use publicly, for record-keeping purposes and continued development, by emailing ihrhrt@who.int