## Slide 1: Laboratory sample management
B7.1
Speaker name

## Slide 2: Introduction
This learning resource is part of the Rapid Response Team Advanced Training Package (RRT ATP) especially geared to RRT members.
Based on an all-hazard approach, the programme aims to provide RRT members with the advanced knowledge, skills, attitudes (KSA) and tools needed to early detect and effectively respond to a public health event.
The RRT ATP is a component of the Rapid Response Teams Training Programme.

## Slide 3: Notes to facilitators:
Some slides of this presentation are hidden. Make sure you review the content of the presentation and decide whether you need to use the entire content of this presentation or not, based on your context, your target learning needs in this specific content area, and the time available for this presentation.
Recommendation: for a 30’ timeslot do not exceed 15 to 20 slides, for a 60’ timeslot 30 to 40 slides.
Within this presentation you may find additional slides with “Notes to facilitators”: these will prompt you to complete and/or customize the content using your country-tailored information.

## Slide 4
At the end of this module, you should be able to :
Identify key actions to be taken before collecting a laboratory sample from suspected case
Determine the type of sample to be collected from suspected case
Describe sample management procedures
Collect laboratory samples taking the appropriate IPC measures
Properly implement decontamination and waste management after sample collection
Properly prepare samples for transport.
Learning objectives

## Slide 5: Outline
    National laboratory sample management system
    What you need to know before you go to the field
    What samples to collect?
    Sample collection steps
    Sample transport
    Documentation
    Sample storage – general recommendations
    Scenario-based activities
    References and guidelines
    Additional training resources
Graphic adapted from: Outlook India

## Slide 6
1. National laboratory sample management system

## Slide 7
Define the cause and magnitude of the public health event
Determine which sample types are required to confirm the cause of the outbreak
Decide who on the investigation team will be in charge of laboratory specimens:
  Will you need someone with experience taking blood or nasopharyngeal, Cerebrospinal fluid (CSF), animal or environmental samples?
  Who on the investigation team will gather the necessary equipment, sample containers, transport media and packaging and transport supplies
Identify the referral laboratories:
  This may be a national laboratory, an international laboratory, an animal or environmental laboratory.
  Will field testing/Rapid Detection Tests (RDTs) be performed?
At the planning phase :
What you need to know before you go to the field

## Slide 8
2. What you need to know before you go to the field

## Slide 9
Define the cause and magnitude of the public health event
Determine which sample types are required to confirm the cause of the outbreak
Decide who on the investigation team will be in charge of laboratory specimens:
  Will you need someone with experience taking blood or nasopharyngeal, Cerebrospinal fluid (CSF), animal or environmental samples?
  Who on the investigation team will gather the necessary equipment, sample containers, transport media and packaging and transport supplies
Identify the referral laboratories:
  This may be a national laboratory, an international laboratory, an animal or environmental laboratory.
  Will field testing/Rapid Detection Tests (RDTs) be performed?
At the planning phase :
What you need to know before you go to the field

## Slide 10
3. What samples to collect?

## Slide 11: Why is it essential to communicate with the laboratory before collecting the sample?
In some cases, you will know what sample you will take before you set off, other times you decide once you have more information.
It is important to communicate with the referral laboratory for the following reasons:
  To know what tests the laboratory will perform
  They can tell you what the sample requirements are (volume, transport temperature, labeling, etc.)
  To inform them of the sample types and numbers being sent and expected delivery time

## Slide 12
Use the following syndromes to assist in identifying the type of samples which may be collected:
  Acute diarrheal syndrome
  Acute haemorrhagic fever syndrome
  Acute jaundice syndrome
  Acute respiratory syndrome
  Acute neurological syndrome
  Acute dermatological syndrome
  Acute ophthalmological syndrome
  Acute systemic syndrome
Ensure there is someone on the team who is trained in the sample collection techniques required.
Where possible, take samples before the patient is treated with antibiotics
What samples to collect? (1)
Notes: Notes for facilitators: the syndromic approach can guide the RRT team members in identifying the apparently most adequate sample types according to available data. However one syndrome does not exclude others. This is especially true for the «acute systemic syndrome».

## Slide 13
Acute diarrhoeal syndrome
Dysenteric syndrome
fever, bloody and/or mucoid stools
Stool
Blood
See Acute Haemorrhagic Fever Syndrome
Clinical presentation, history of the illness, epidemiological context, vaccination status…
Collection should be done before any antibiotic/antiparasitic treatment
Collection process, container, transport medium, temperature during storage and transport,
delay before analysis, etc. may vary according to the suspected pathogen and tests performed
The laboratory is able to provide you with those information
Diarrhea
no fever, abundant watery stools
Acute onset of diarrhea
AND
Severe illness
AND
Absence of known predisposing factor

## Slide 14
Acute haemorrhagic fever syndrome
Suspected pathogen:
Arenaviridae (Lassa, Lujo, Chapare, Guanarito, Junín, Machupo and Sabiá)
Bunyaviridae (Nairovirus, Phlebovirus and Hantavirus)
Filoviridae (Ebolavirus and Marburgvirus)
Flaviviridae (yellow fever, dengue, Omsk haemorrhagic fever, and Kyasanur forest disease)
Malaria
Relapsing fever
Etc.
Capillary blood
Rapid diagnostic test where possible
Venous blood
Whole blood in EDTA coated tube
Transport and storage at 2-8°C
Oral or nasal swab
Transport and storage at 2-8°C
Blood collection is possible
No
Yes
More sensitive and/or specific test needed
/!\ Maximum precautions are required during collection, storage and transport of the sample
Acute onset of fever of less than 3 weeks duration AND any two of the following: | 
Haemorrhagic or purpuric rash Epistaxis Haemoptysis | Blood in stool Other haemorrhagic symptoms
AND absence of known predisposing factors | 

## Slide 15
Acute jaundice syndrome
Acute onset of jaundice
AND
Severe illness
AND
Absence of known predisposing factors
Suspected pathogen:
Hepatitis A and E
Malaria
VHF
Typhoid fever
Leptospirosis
Sepsis syndrome
Etc.
Blood
Blood culture*
Serum
Capillary blood
See Acute Haemorrhagic Fever Syndrome
Mid-stream urine*
*Collection should be done before any antibiotic treatment
Clinical presentation, history of the illness, epidemiological context, vaccination status…
Collection process, container, transport medium, temperature during storage and transport,
delay before analysis, etc. may vary according to the suspected pathogen and tests performed
The laboratory is able to provide you with those information

## Slide 16
Acute neurological syndrome
Acute neurological dysfunction with one or more of the following:
Deterioration of mental function
Acute paralysis
Convulsions
Signs of mental irritation
Involuntary movements
Other neurological symptoms
AND
Severe illness
AND
Absence of known predisposing factors
Guillain Barré syndrome and poliomyelitis
Bacterial*, viral, fungal or parasitical meningoencephalitis
Rabies
Clinical presentation, history of the illness, epidemiological context, vaccination status…
Stool
Blood
Throat swab
Cerebrospinal fluid
Saliva
*Collection should be done before any antibiotic/antiparasitic treatment
Collection process, container, transport medium, temperature during storage and transport,
delay before analysis, etc. may vary according to the suspected pathogen and tests performed
The laboratory is able to provide you with those information
Notes: Notes for facilitators: Rabies usually gets overlooked and should be seriously considered in case of acute neurological syndrome in rabies endemic areas.

## Slide 17
Acute respiratory syndrome
Acute onset of cough OR respiratory distress
AND
Severe illness
AND
Absence of known predisposing factors
Viral infection:
SARS
Influenza
RSV
Hantavirus pulmonary syndrome
Etc.
Upper respiratory tract infection:
Pertussis
Diphtheria
Streptococcal pharyngitis and scarlet fever
Etc.
Pneumonia
with epidemic potential:
Pneumonic plague
Legionellosis
Respiratory anthrax
Etc.
Upper
respiratory
tract
sample
Lower
respiratory
tract
sample
Clinical presentation, history of the illness, epidemiological context, vaccination status…
Blood
*Collection should be done before any antibiotic treatment
Urine
Stool
Collection process, container, transport medium, temperature during storage and transport,
delay before analysis, etc. may vary according to the suspected pathogen and tests performed
The laboratory is able to provide you with those information
Bacterial infection*

## Slide 18
Acute dermatological syndrome
Acute febrile illness with rash OR skin manifestations
AND
Absence of known predisposing factors
Chickenpox
Monkeypox
Etc…
Measles
Rubella
Typhus
Etc…
Cutaneous anthrax*
Etc…
Blood
Urine
Upper respiratory
tract swab
Skin lesion
Clinical presentation, history of the illness, epidemiological context, vaccination status…
*Collection should be done before any antibiotic treatment
Measles and
Rubella
Collection process, container, transport medium, temperature during storage and transport,
delay before analysis, etc. may vary according to the suspected pathogen and tests performed
The laboratory is able to provide you with those information

## Slide 19
Acute ophthalmological syndrome
Acute onset of conjunctivitis with or without
sub-conjunctival hemorrhages
AND
Absence of known predisposing factors
Suspected diseases:
Epidemic adenoviral keratoconjunctivitis
Hemorrhagic conjunctivitis
Ect…
Blood
Tube ± clot activator
± separator gel
Transport and store at 2-8°C or
ambient temperature <48h
Upper respiratory
tract swab
Viral transport medium
Clinical presentation, history of the illness, epidemiological context…
Conjunctival swab
Viral transport medium

## Slide 20
Acute “systemic” syndrome
Viruses
Viral hemorrhagic fevers
Chikungunya
ONNV
Zika virus
Hantavirus
West Nile virus
Typhus
SRAS
Etc.
Bacteria*
Coxiella
Brucellosis
Leptospirosis
Rickettsiosis
Salmonellosis and typhoid fever
Plague
Anthrax
Borreliosis
Etc.
Protozoa*
Trypanosoma brucei
Malaria
Leishmaniosis
Etc.
Acute febrile illness characterized by symptoms from several body systems, with three or more of the following:
AND
absence of predisposing factors
Stool
Urine
Cutaneous
specimen
Blood
Respiratory
specimen
Clinical presentation, history of the illness, epidemiological context, vaccination status…
*Collection should be done before any antibiotic/antiparasitic treatment
Collection process, container, transport medium, temperature during storage and transport,
delay before analysis, etc. may vary according to the suspected pathogen and tests performed
The laboratory is able to provide you with those information
Appetite and weight loss Nausea and vomiting Diarrhea Abdominal discomfort | Sweat and chills Headache Arthralgia, myalgia and back pain Rash
Notes: Notes for facilitators: sample types mentioned here are somehow easy to collect. Other samples, including more invasive samples like CSF, may be needed. For instance, refer to the acute neurological syndrome flowchart if the clinical history and epidemiological context suggest a neurological affection.

## Slide 21: What samples to collect - Summary
REMEMBER: If in doubt, ask the laboratory!
Diarrhoeal |  | Conjunctival swab
Haemorrhagic Fever |  | Stool
Jaundice |  | Respiratory track sample
Neurological |  | Blood
Respiratory |  | Saliva
Dermatological |  | Cerebrospinal fluid
Ophthalmological |  | Urine
Systemic |  | Lesion swab or crust

## Slide 22
What samples to collect - Summary

## Slide 23
4. Sample collection steps

## Slide 24
Protect yourself: put on appropriate personal protective equipment (PPE) based on risk assessment
Get ready: label containers and forms and assemble all equipment and materials before approaching the patient
Collect sample: use sterile technique and safety precautions
Sample Transportation: prepare sample container for transport
Clean up: manage waste, spills and accidental exposures
Sample collection and transportation

## Slide 25
WASH
YOUR HANDS BEFORE AND AFTER PATIENT CONTACT AND BETWEEN PATIENTS
THE MINIMUM RECOMMENDATION IS UNIVERSAL PPE. THIS INCLUDES GLOVES, GOWN AND EYE PROTECTION
WEAR FULL PPE IF, FOR INSTANCE, A VIRAL HAEMORRHAGIC FEVER OR PANDEMIC FLU IS SUSPECTED
Graphics adapted from: RRT lab module
Protect yourself
Notes: Notes for facilitators: The level of PPE should be based on a risk assessment of the activity being performed and mode of transmission of the suspected pathogen. Refer to next slides.

## Slide 26
To decide which level of PPE will provide enough protection :
Protect yourself
Notes: To decide which level of PPE will provide enough protection for the wearer, consider: The syndrome, the mode of transmission and the activity being performed.

## Slide 27
The PPE level of protection should be appropriate for the pathogen and the activity being performed.
Minimum PPE recommendations:
Blood-borne/Body Fluid Pathogens:
  Low Risk: gloves, gown, goggles
  Medium Risk: gloves, gown, face shield
  High Risk: double gloves, gown, full respiratory protection, boots.
Airborne Pathogens:
  Low Risk: gloves, gown, goggles, partial respiratory protection*
  Medium Risk: gloves, gown, goggles, full respiratory protection**
  High Risk: double gloves, gown, full respiratory protection.
Vector Borne Pathogens:
  Use PPE appropriate for Blood-borne/Body Fluid Pathogens;
  Insect repellant should also be used.
* Partial respiratory protection = surgical mask
** Full respiratory protection = N95 & face shield or Power Air Purifying Respirator System - PAPR)
PPE Levels
Protect yourself
Notes: Notes for facilitators: Some of the risk may come from the activity being carried out. Suggestion of group discussion or exercise: come up with examples (pathogen and activity) for some risk groups in the context of an RRT outbreak investigation in the field and discuss if the PPE recommendations are appropriate.

## Slide 28
UNIVERSAL PPE
FULL PPE
BLOOD BORNE
AIR BORNE
N-95 Mask
Double gloves
Face shield
PAPR system
Boots
Gloves
Gown
Eye protection (goggles)
RRT lab module
RRT lab module
RRT lab module
RRT lab module
RRT lab module
RRT lab module
G.Pellegrini, CDC
G.Pellegrini, CDC
PPE Levels
Protect yourself
Notes: Notes for facilitators:
reflect with the audience on what to do if adequate PPE is not available
the levels of protection on the 2 pictures on the right are equivalent

## Slide 29
To ensure respiratory protection you may use:
Surgical Masks
  Protects the wearer from droplet transmission.
  Does not protect the wearer from aerosolized agents
  Cannot be reused
N95 Masks
  User should be fit tested and clean shaven (subject to change based on fit testing resource availability and cultural practices)
  Humidity & Moisture reduces efficiency
  Cannot be reused
  Are difficult to wear for long periods (>2hours)
Note: None of these systems protect from toxic chemical gases or vapors.
Respiratory protection
Protect yourself
Notes: Note: WHO COVID-19 Technical Guidance continues to be updated, so please check WHO website for the most up to date guidance prior to giving this training

## Slide 30
Introduce yourself to the patient and explain what you will do and why.
Record keeping is crucial;
  Collect epidemiological information about patient and fill out on the case investigation form (CIF) or standard national request form;
  Label the form and the primary container with a minimum of three identifiers: sample name or unique ID, date of collection, time of collection and sample collector’s initials.
Ensure you have a helper nearby to assist you with PPE and additional equipment.
Graphic adapted from: RRT lab module
Get ready

## Slide 31
Things to consider:
A person trained in phlebotomy should take the sample;
Does the laboratory need plasma or serum?
  Tube with anticoagulant (EDTA, heparin) for plasma;
  Tube ± clot activator for serum.
  CAUTION! there is no standard for color of tube caps.
Did you know?
Gently mix tubes after collection to mix blood;
Red cells lyse when samples are stored at temperatures that are too high or too low;
Serum is needed for serology testing;
To test for some pathogens, a second sample may be required during convalescence;
Blood for culture must not be allowed to clot and should not be frozen;
If a venous blood sample cannot be taken, a finger stick may be collected in some instances.
Which blood sample?
Contact the laboratory to confirm the sample type, but also: amount needed, tube to be used, storage and/or transport temperature, etc.
RRT lab module
Blood samples

## Slide 32
  Only persons experienced in taking stool samples should take the samples;
  Collect sample before treatment, or take note if the patient has been given antibiotics;
  Cholera RDTs can be used to screen samples in the field
  Appropriate transport media preserves the samples for 48 to 72 hours;
    Cary-Blair
    Amies/Stuart
    Para-Pak®
To collect a stool sample:
~5g of stool should be transferred into a clean, leak-proof screw cap container and tape closed with parafilm.
Alternatively, stool may be collected directly with a proper swab.
A rectal swab may be useful for infants and small children
Things to consider:
Stool samples

## Slide 33
Only a person who is trained and experienced in CSF collection should take the sample;
Lumbar puncture should not be performed at site of a localized skin lesion or in case of other counterindications;
Aseptic technique strictly followed to prevent infection and sample contamination;
Trans-Isolate transport media (TI) should be used for culture samples;
Do not refrigerate samples if culture is required;
  E.g. for bacterial meningitis.
Thermo Fisher Scientific
Cerebrospinal Sample Fluids (CSF)
Things to consider:

## Slide 34
Only persons experienced in taking throat and nasopharyngeal swabs should take samples;
  Sterile swab tube for each swab;
  Appropriate transport media should be included in the tube;
    For culture this may include Amies or Stuart media;
    For other tests this may be a viral or universal transport media (VTM/UTM)
Things to consider:
Oropharyngeal and Nasopharyngeal Swabs (1)

## Slide 35
Graphic adapted from: CDC Technical Guidance
Aviva
Nasopharyngeal (NP) swab
  Insert flexible wire shaft swab through the nares parallel to the palate (not upwards) until resistance is encountered or the distance is equivalent to that from the ear to the nostril of the patient, indicating contact with the nasopharynx. Swab should reach depth equal to distance from nostrils to outer opening of the ear
  Gently rub and roll the swab (leave swab in place for several seconds to absorb secretions)
  Slowly remove swab while rotating it
Oropharyngeal (OP) swab
  Insert swab into the posterior pharynx and tonsillar areas
  Rub swab over both tonsillar pillars and posterior oropharynx and avoid touching the tongue, teeth, and gums
Oropharyngeal and Nasopharyngeal Swabs (2)
Notes: Note: WHO COVID-19 Technical Guidance continues to be updated, so please check WHO website for the most up to date guidance prior to giving this training

## Slide 36
Watch WHO video on Nasopharyngeal and Oropharyngeal swab collection (WHO-TRA COVID-19 diagnosis specimen collection 12FEB2021):
https://youtu.be/jh6Is9oPyyw
Oropharyngeal and Nasopharyngeal Swabs (3)

## Slide 37
The RRT may be responding to a death report:
  Protect yourself even if it is a post-mortem sample.
Sample types depend on the disease and may include:
  A buccal (oral fluid) swab
  Skin or tissue biopsy;
  Arterial or cardiac blood draws;
  Rectal swabs.
Post-mortem samples

## Slide 38
You may respond to a report of a sick person, but when you start asking questions you suspect the etiology may be animal or environmental related.
Environmental samples may include:
  Water samples;
  Soil samples;
  Food samples;
  Filtered air samples.
Animal samples may include:
  Insects;
  Animal biopsies or carcass;
  Animal blood, feces or swab samples.
Always wear appropriate PPE for sample collection.
Animal and environmental samples

## Slide 39
http://www.who.int/malaria/areas/diagnosis/rapid-diagnostic-tests/about-rdt/en/
Rapid tests can include lateral flow immunoassays or molecular techniques.
They may be used as either diagnostic or screening tools and can be very helpful in field settings;
Depending on the country, the following may be diagnosed based on the result of an RDT; e.g.
  Malaria
  Dengue
  COVID-19...
Other diseases may use RDT initially but require laboratory. Confirmation by culture, serology or molecular testing; e.g. Cholera.
New RDTs are being developed all the time and new devices may be introduced during response situations.
  For example, during the 2014 Ebola outbreak, both lateral flow immunoassays and GeneXpert cartridges were developed and tested.
Zoom on Rapid Diagnostic Tests (RDTs)

## Slide 40
5. Sample transport

## Slide 41
  Put the sample in the appropriate container based on transportation (international vs. national) and type of test used.
  Consider the temperature requirements needed for sample shipment based on type of test used and the expected transportation time
Key considerations
Notes: Note to facilitator: Briefly summarize key bullets
Additional Information on temperature requirements (https://www.cdc.gov/coronavirus/2019-ncov/lab/biosafety-faqs.html)
Specimens should be shipped at 2-8 degrees C with ice packs. If the specimen is frozen, ship overnight on dry ice.
The primary receptacle and the secondary packaging should maintain their integrity at the temperature of the refrigerant used as well as the temperatures and the pressures which could result if refrigeration were lost.
Packages containing dry ice should be designed and constructed so as to prevent the buildup of pressure and to allow the release of gas that could rupture the packaging.
Specimens for virus isolation and nucleic acid detection purposes should be tested as soon as possible. (http://www.chinacdc.cn/en/COVID19/202003/P020200308322036088669.pdf)
Specimens to be tested within 24 hours can be stored at 4 °C
Those that cannot be tested within 24 hours should be stored at -70 °C or below (specimens may be temporarily stored in -20 °C refrigerators in the absence of -70 °C storage condition). Serum can be stored at 4 °C for 3 days and below -20 °C for a longer period.
A special depot or cabinet is required to store specimens separately. Repeated freeze-thaw cycles during specimen transportation should be avoided.

## Slide 42
  Category A: an infectious substance which is transported in a form that, when exposure occurs, is capable of causing permanent disability, life-threatening or fatal disease in otherwise healthy humans or animals (Ex. TB culture or virus culture)
  Shipping label:
    UN2814 - INFECTIOUS SUBSTANCE AFFECTING HUMANS (and animals)
    UN2900 - INFECTIOUS SUBSTANCE AFFECTING ANIMALS only
  Category B: an infectious substance that does not fit the criteria for inclusion in category A (Ex. TB sputum or nasal swab from suspected COVID-19 patient)
  Shipping label:
    UN3373 BIOLOGICAL SUBSTANCE CATEGORY B
  Classification of substances:
International sample transport
Notes: Note: WHO COVID-19 Technical Guidance continues to be updated, so please check WHO website for the most up to date guidance prior to giving this training
Note to facilitator: Briefly summarize key bullets

## Slide 43
For international sample transport, consider:
Proper Shipping Name (PSN) of Infectious Substance
UN Number of Infectious Substance.
Name & Address of Shipper & Receiver
Emergency Name & Telephone Number of a Responsible Person (may be written on the airway bill for Cat B packages)
UN 3373
INFECTIOUS SUBSTANCE,
AFFECTING HUMANS
UN 2814
BIOLOGICAL SUBSTANCE,
CATEGORY B
ISST Training Programme
dry ice as coolant
UN1845
Net quantity ____kg
Indicators of dry ice (if applicable) including PSN, UN number and net quantity used
RRT lab module
RRT lab module
Sample Transport Marks
International sample transport
Notes: Notes for facilitators: «marks» are what need to be written on the shipping box: address, etc.

## Slide 44: International sample transport regulations critical documents
An itemized list of contents must be enclosed between the secondary & outer packaging.
All shipments by air must be accompanied by a properly filled in Air Way Bill. Cat A Substances also require a Dangerous Goods Declaration.
It is the responsibility of the shipper to check whether customs permits are necessary. Common documents requested by customs include:
  Export and/or Import permits
  Custom invoice indicating;
    Contents (e.g. Infectious substance-human blood/urine/serum)
    No commercial value Customs Declaration
Material Transfer Agreement from shipping institution may be necessary.
Always check with the carrier for advice on necessary documents. Carriers often refuse or delay shipments due to improperly filled or missing paperwork!
To comply with international sample transport regulations, consider:
Notes: Notes for facilitators: Import permits may be the responsibility of the receiving laboratory.

## Slide 45
  The triple packaging contains:
  Primary receptacle
  Watertight, leak-proof receptacle containing the sample.
  Package with enough absorbent material to absorb all fluid in case of breakage or leakage and to stabilize samples during transport.
  Secondary packaging
  Durable, watertight, leak-proof packaging to enclose and protect the primary receptacles.
  Several cushioned primary receptacles may be placed in one secondary packaging.
  Tertiary packaging
  Secondary packaging is placed in outer packaging with suitable cushioning material.
  May contains ice or dry ice (if necessary) to maintain sample temperature.
  Contains documentation.
Internationally, only packaging tested & approved using Packing Instruction 620 should be used for Category A shipments. These packages are marked with a UN packaging symbol.
Packing Instruction 650 may be used to guide packaging of Cat B substances.
4G/CLASS 6.2/02
F/BVT 312103
u
n
Graphics adapted from: ISST Training Programme
Triple packaging
International sample transport
Notes: Note: WHO COVID-19 Technical Guidance continues to be updated, so please check WHO website for the most up to date guidance prior to giving this training
Notes to facilitators: Don’t enclose dry ice in airtight containers! Using dry ice is not common for outbreak investigation in the field.

## Slide 46
  Many countries utilize modified sample transport systems to meet their daily needs.
  Shipping containers can be disinfected and are reusable.
  The Golden Rule for any sample transport is: triple packaging protects the worker, the sample and the environment, as explained below:
  Primary Package: is the sample container which is often placed within a sealable bag or a plastic container, with enough absorbent material to contain a spill.
  Secondary Package: is a sturdy waterproof sealable container used to protect the samples during transport and can contain multiple primary packages.
  Tertiary Package: can contain multiple secondary packages. It functions to regulate sample temperature, hold required documentation and protect the environment.
Graphics adapted from: RRT lab module
National sample transport
Notes: Notes to facilitators:
Primary package can be placed in sealable bag or plastic container to limit contamination of the workers from the outer surface of the primary package. This was a recommended practice when shipping a Ebola suspected sample.
Primary container must be correctly marked with a minimum of three identifiers: sample name or unique ID, date of collection, time of collection.
Tertiary package must be correctly marked and labelled: refer to slides 7-8.

## Slide 47
Ensure sharps are disposed in a suitable container to minimize the risk of injury
RRT lab module
RRT lab module
Disinfect materials at source as much as possible using appropriate disinfectant:
    Bleach (1000 parts per million [ppm] (0.1%) for general surface disinfection and 10 000 ppm (1%) for disinfection of blood spills)
    62–71% ethanol...
Be sure to disinfect sharps containers
Double bag and sealed hazardous waste
Take hazardous waste to location where it can be properly disinfected and disposed of
The RRT should manage all waste they create to protect the community and environment.
Clean up
Notes: Notes for facilitators: 10% hypochlorite is 10,000 ppm. Hypochlorite solution (bleach) has to be freshly prepared, unless the hypochlorite solution includes a stabilizer.

## Slide 48
Depending on what is available on site, infectious waste can be disposed of in the following ways:
Incineration
Containment & burial
Infectious waste should be disinfected before disposal:
Autoclave
Chemical disinfection
Waste disposal
Notes: Notes for facilitators: Disposal and disinfection methods are effective if equipment (e.g. autoclave, incinerator) or reagents (e.g. hypochlorite) are properly maintained/prepared and used strictly in accordance with appropriate protocols.
Incineration, due to high temperatures in the burn pit, can also be an effective disinfection method if used correctly. However, incineration, particularly in an open pit, is a much less controlled environment than autoclave and requires longer heating times and higher temperatures to be effective in disinfecting. Also keep in mind that:
an open fire has the potential to disperse viable organisms in the air currents;
burning waste treated with chlorine could generate dioxins which are carcinogenic;
burning certain types of plastics can release harmful chemicals.
Autoclaving provides a more controlled environment but effectiveness can be compromised by overloading, obstructing the circulation of steam, bags sealed too tightly, trying to autoclave sealed containers, etc.

## Slide 49
  Move away from the spill area;
  Alert others in the area of the spill;
  Treat any potential exposures;
    Disinfect clothing splashes;
    Remove contaminated PPE;
    Seek medical attention for those exposed.
  Contain the spill;
    Cover with absorbent materials;
    Disinfect with an appropriate disinfectant, such as 10% hypochlorite freshly prepared;
    Remove sharps.
  Collect the waste;
    Gather the waste for proper disposal.
  Report the incident.
Steps to ensure response to a spill of blood or bodily fluids are:
Spills and accidental exposure

## Slide 50
6. Documentation

## Slide 51
Documentation of each sample collected is very important.
WHO Laboratory Quality Stepwise Implementation (LQSI) tool
https://extranet.who.int/lqsi/content/develop-request-form-laboratory-testing
Documentation

## Slide 52
7. Sample storage – general recommendations

## Slide 53
  If samples are not packaged and shipped correctly, the laboratory may not accept them;
  If samples cannot be transported immediately, they should be stored at the appropriate temperature;
  Contact the laboratory to check appropriate storage and transport temperatures;
  Keep the laboratory informed of any delays and of any deviation from requirements (wrong storage temperature, etc.)
Sample Type | Test | Transport Media | Recommended Temperature
Plasma | PCR | N/A | 2 to 8ºC
Serum | Serology | N/A | 2 to 8ºC
Swab | PCR | UTM or VTM | 2 to 8ºC
Swab | Culture | Amies or Cary Blair Media | 2 to 8ºC
CSF | Culture | TI Media | Ambient
Stool | Culture | Cary Blair Media | 2 to 8ºC
Key Points:
Sample storage – general recommendations
Notes: Notes for facilitators:
Sample transport will be discussed in further detail in the sample transport module.
Table is indicative. Depending on the laboratory test and the shipment time, different transport media and temperature may be preferable.
The main idea is to always check with the laboratory.

## Slide 54
8. Scenario-based activity

## Slide 55
  The RRT was conducting contact tracing in a community during Measles outbreak when a known contact revealed that they developed a fever and skin rash in the last evening.
Scenario 1

## Slide 56
  What minimal PPE should be used for sample collection of this individual?
  What processes would you implement to ensure succesful collection, storage, and transport of the sample collected?
  What follow-up measures can be taken to ensure sample was received?
Scenario 1 - Questions

## Slide 57
1. What minimal PPE should be used for sample collection of this individual?
  Gloves, medical mask.
2. What processes would you implement to ensure successful collection, storage, and transport of the sample collected?
  Put the sample in the appropriate container based on transportation (international vs. national) and type of test used
  Ensure proper labeling of samples and containers, and include adequate documentation.
  Consider the temperature requirements needed for sample shipment based on type of test used
  If samples cannot be transported or tested immediately, they should be stored appropriately (see next slide);
  It is your responsibility to remove hazardous waste and make it safe.
3. What follow-up measures can be taken to ensure sample was received?
  Notify the laboratory in advance of the number of samples and their expected delivery time
  Check with the carrier to ensure there are no issues with the shipment (e.g. customs)
  Make sure the carrier and laboratory can contact you if a problem arises or if they have questions concerning the sample shipment.
Scenario 1 - Answers

## Slide 58
  The Rapid Response Team visited a local health care facility to investigate a sick man that health care personnel suspected having COVID-19. The patient was ill with fever, dry cough, and shortness of breath.
Scenario 2

## Slide 59
  What minimal PPE should be used for sample collection of this individual?
  What processes would you implement to ensure successful collection, storage, and transport of the sample collected?
  What follow-up measures can be taken to ensure sample was received?
Scenario 2 - Questions

## Slide 60
1. What minimal PPE should be used for sample collection of this individual?
  Gloves, N95 or medical mask, apron, gown, eye protection.
2. What processes would you implement to ensure successful collection, storage, and transport of the sample collected?
  Put the sample in the appropriate container based on transportation (international vs. national) and type of test used
  Ensure proper labeling of samples and containers and include adequate documentation.
  Consider the temperature requirements needed for sample shipment based on type of test used
  If samples cannot be transported or tested immediately, they should be stored appropriately (see next slide);
  It is your responsibility to remove hazardous waste and make it safe.
3. What follow-up measures can be taken to ensure sample was received?
  Notify the laboratory in advance of the number of samples and their expected delivery time
  Check with the carrier to ensure there are no issues with the shipment (e.g. customs)
  Make sure the carrier and laboratory can contact you if a problem arises or if they have questions concerning the sample shipment.
Scenario 2 - Answers

## Slide 61
Addition to answer 2:
Recommended conditions for international shipment of specimens referred for Covid-19 testing (Testing guidance as of 14/5/2020).
Scenario 2

## Slide 62
Sample collection and time between collection and processing directly affect the quality and reliability of the laboratory results
Consider the following:
  Notify the laboratory in advance of the number of samples and their expected delivery time
  If samples cannot be transported or tested immediately, they should be stored appropriately;
  It is your responsibility to remove hazardous waste and make it safe.
  If in any doubt, discuss your plans with the laboratory
  Record all steps and keep the laboratory informed.
Notes: Note: WHO COVID-19 Technical Guidance continues to be updated, so please check WHO website for the most up to date guidance prior to giving this training

## Slide 63
  You have questions? Contact the laboratory and/or the carrier!
  Make sure the carrier and laboratory can contact you if a problem arises or if they have questions concerning the sample shipment
  Check with the carrier to ensure there are no issues with the shipment (e.g. customs)
  Ensure proper labeling of samples and containers, and include adequate documentation.
Key messages
Notes: Note: WHO COVID-19 Technical Guidance continues to be updated, so please check WHO website for the most up to date guidance prior to giving this training
Notes for facilitators: Private carriers (e.g. airlines) have the right to refuse to carry goods and may hold shipments for extended periods prior to transport.

## Slide 64
9. References and guidelines

## Slide 65
WHO Laboratory biosafety manual, 4th edition: Personal protective equipment
https://www.who.int/publications/i/item/9789240011410
UN Recommendations on the Transport of Dangerous Goods, 2017 http://www.unece.org/trans/danger/publi/unrec/rev20/20files_e.html
ICAO Technical Instructions
https://www.icao.int/safety/DangerousGoods/Pages/technical-instructions.aspx
Specimen labeling, storage & handling, CDC
https://www.cdc.gov/urdo/downloads/specstoragehandling.pdf
WHO Guidance on regulations for the transport of infectious substances 2017–2018
http://www.who.int/ihr/publications/WHO-WHE-CPI-2017.8/en/
WHO Infectious Substances Shipping Training - a course for shippers
http://www.who.int/ihr/i_s_shipping_training/en/

## Slide 66
European Agreement on the International Carriage of Dangerous Goods by Road (ADR), 2017 www.unece.org/trans/danger/publi/adr/adr2017/17contentse0.html
Regulations on the International Carriage of Dangerous Goods by Rail (RID), 2017
http://otif.org/en/?page_id=174
Guideline for Disinfection and Sterilization in Healthcare Facilities, 2008, CDC
https://stacks.cdc.gov/view/cdc/11560
Guidelines for the collection of clinical specimens during field investigation of outbreaks, WHO/CDS/CSR/EDC/2000.4
http://www.who.int/ihr/publications/WHO_CDS_CSR_EDC_2000_4/en/
CDC Infectious Diseases Laboratories Test Directory, https://www.cdc.gov/laboratory/specimen-submission/list.html
COVID-19 Specimen Collection – Nebraska Medical Center, https://www.youtube.com/watch?v=7g4aeMDe_tc&feature=youtu.be
Notes: Note: WHO COVID-19 Technical Guidance continues to be updated, so please check WHO website for the most up to date guidance prior to giving this training

## Slide 67
10. Additional learning resources

## Slide 68
SARS-CoV- Antigen Rapid Diagnostic Test training package
https://extranet.who.int/hslp/content/sars-cov-2-antigen-rapid-diagnostic-test-training-package

## Slide 70
WHO Health Security Learning Platform - Training Materials
These WHO Training Materials are © World Health Organization (WHO) 2022. All rights reserved.
Your use of these materials is subject to the “WHO Health Security Learning Platform, Training Materials – Terms of Use”, which you accepted when downloading them and which are available on the Health Security Learning Platform at: https://extranet.who.int/hslp
Should you adapt, modify, translate, or in any other way revise the contents of these materials, you shall not imply that WHO is any way affiliated with such modifications and shall not use the WHO name or emblem in such modified materials.
Should you adapt, modify, translate, or in any other way revise the contents of these materials, you shall acknowledge the source of the material providing the following attribution: “These training materials are a modified version of the Rapid Response Teams Advanced Training Package (available at: https://extranet.who.int/hslp/), which is © the World Health Organization (WHO), 2022, and used with permission from WHO. WHO disclaims any responsibility for any modifications to, or revisions of, the WHO copyrighted materials.”
Further, please inform WHO of any modifications of these materials that you use publicly, for record-keeping purposes and continued development, by emailing ihrhrt@who.int