## Slide 1: Monitoring Equipment Used in the Microbiology Laboratory
<number>
Notes: <number>

## Slide 2: Equipment - Microbiology
<number>
Monitor temperatures of:
  incubators
  refrigerators
  freezers
Perform function checks for:
  pipettes
  autoclaves
  pH meter
  weights and measures
Maintain records
Notes: <number>

## Slide 3
<number>
Notes: <number>

## Slide 4: Sterilization
<number>
Sterile
media
reagents
materials
Safe
disposable
waste
Preparing
media
reagents
materials
Contaminated waste
Notes: <number>

## Slide 5: Two Stage Sterilization Controls
<number>
Process control
  Chemical indicators
  Bacteriological indicators
Sterile products control
  Growth test
Notes: <number>

## Slide 6: Sterilization indicators
<number>
Notes: <number>

## Slide 7: Sterility Indicators
<number>
Chemical indicators
Temperature for sterilization have been met. Do not address time or pressure
Biological indicators
Temperature, time and pressure for sterilization have been met
NOTE:
Neither indicator is a guarantee of sterilization if:
Autoclave is overpacked
Broth volumes are too large
Notes: <number>

## Slide 8: Sterilization Logbook
<number>
Notes: <number>

## Slide 9: Microscopes
<number>
Keep lens clean
Have at least one oil immersion lens (X100)
Use spring loaded lens
Keep non-immersion lens free of oil
Do not allow sample to migrate above the lens
Maintain Kohler Illumination
Notes: <number>