## Slide 1
Equipment

## Slide 2: Learning Objectives
At the end of this module, you will be able to:
List factors to consider prior to purchasing equipment for the laboratory.
Manage the selection and acquisition of new equipment.
Describe the requirements for a preventive maintenance program for equipment.
Provide a rationale for developing a preventive maintenance programs in your laboratory.
Explain how to retire old or outdated equipment.

## Slide 3: Scenario
“The reader fails while performing ELISA / EIA tests. There isn’t a documented procedure for troubleshooting, the maintenance log has not been updated for 2 years, and the manufacturer’s instructions are missing.”
What should you do? Why?
What should you have done earlier ?
What you would do if this happened in your laboratory?
Notes: <number>

## Slide 4: The Quality Management System
Organization
Personnel
Equipment
Purchasing & Inventory
Process Control
Information Management
Documents & Records
Occurrence Management
Assessment
Process Improvement
Customer Service
Facilities & Safety
Notes: <number>

## Slide 5: Equipment Management Benefits
Performance high level
Test results
Variation/ Time
Lowers repair costs
Lengthens lifespan

## Slide 6: Equipment Management Benefits
Reduces interruption of services
Increases safety
Greater customer satisfaction

## Slide 7: Program Considerations
Retiring equipment/ disposition
Service and repair
Trouble- shooting
Maintenance
Calibration/ performance evaluation
Installation
Selection and acquisition

## Slide 8: Equipment Management Overview
assign responsibilities for all activities
train all personnel on requirements and maintenance needs
monitor equipment management activities:
  ensure all procedures are followed
  review all records routinely
  update procedures as needed

## Slide 9: Selecting and Acquiring Equipment
performance characteristics
cost
reagents
Facility requirements
Equipment needs
Notes: <number>

## Slide 10: Selecting and Acquiring Equipment
easy to use
safety
will it fit?
warranty
language
Notes: <number>

## Slide 11: Acquiring Equipment
purchase, lease, rent, donations
  central acquisition
  bulk procurement
conditions of contract

## Slide 12: Negotiating Equipment Acquisition
wiring diagrams
software information
parts list
operator manual
installation by manufacturer
trial period
Request:

## Slide 13: Before Equipment Installation
confirm vendor’s responsibilities in writing
establish checklist

## Slide 14: Equipment Installation
when possible, have manufacturer install and set up
do not attempt to use prior to proper installation

## Slide 15: Equipment Installation
  verify package contents
  copy software, if part of system

## Slide 16: After Equipment Installation
Inventory Record
Calibration
Verification
Operating Procedures
Maintenance Program
Train ALL Operators

## Slide 17: Equipment Calibration
perform initial calibration
  use calibrators or standards
  follow manufacturer’s instructions
determine frequency of routine calibrations

## Slide 18: Performance Evaluation
Test known samples, analyze data
Validate performance with parallel samples
Establish stability for temperature- controlled equipment
New Equipment

## Slide 19: Function Checks
Monitor instrument parameters:
  periodically, daily, weekly, monthly
  after major instrument repair
Examples:
  incubator temperatures
  wavelength calibration
  autoclave temperature chart

## Slide 20: Preventive Maintenance
routine cleaning
adjustment, replacement of equipment parts

## Slide 21: Implementing a Maintenance Program
assign responsibility
develop written policies and procedures
maintain records
train staff

## Slide 22: Develop a Maintenance Plan
For each piece of equipment establish routine maintenance plan to include:
  frequency of all maintenance tasks
  function checks
  routine replacement of parts
Notes: <number>

## Slide 23: Create an Equipment Inventory Log
Record:
  instrument type, model number, serial number
  location in laboratory
  date purchased
  manufacturer and vendor contact information
  warranty, note expiration date
  spare parts

## Slide 24: Spare Parts Inventory
Include:
record of spare parts
log to track stock
cost and ordering information

## Slide 25: Troubleshooting: What is the source of the problem?
Sample?
Reagent?
Water, Electricity?
Equipment?
Instructions

## Slide 26: When in-house efforts fail:
call manufacturer or other technical expert
look for options to continue service
  obtain back-up instrument from central stores or manufacturer
  refer sample to nearby laboratory

## Slide 27
Do NOT use equipment that does not function properly
WARNING
OUT OF ORDER
DO NOT USE

## Slide 28: Service and Repair
manufacturers
  laboratory must schedule routine manufacturer’s maintenance
  warranty may require repair handled by manufacturer
in-house biomedical service technicians
Notes: <number>

## Slide 29: Retiring Equipment / Disposal

## Slide 30: Retiring Equipment / Disposal
X
X

## Slide 31: Documents
Develop written procedures for:
  routine maintenance
  function checks
  calibration
  troubleshooting
  manufacturer’s service

## Slide 32: Dedicated Log Book
Routine maintenance:
  calibration
  service repair by manufacturer
  all problems
Function checks

## Slide 33: Recording Problems
date problem occurred, equipment removed from service
reason for breakdown or failure
corrective actions taken
date returned to use
change in maintenance or in function checks

## Slide 34: Example of logbook 1

## Slide 35: Example of logbook 2

## Slide 36: Example of logbook 3

## Slide 37: Summary
An equipment management program will address:
  equipment selection
  preventive maintenance
  procedures for troubleshooting and repair
Documents and records will include:
  inventory of all laboratory equipment
  Information provided by the manufacturer on operation, maintenance, and troubleshooting
  records of all preventive maintenance and repair activities

## Slide 38: Key Messages
A well-organized equipment maintenance program provides:
High level of performance and greater confidence in the reliability of results.
Fewer interruptions in test performance, lower repair costs, and elimination of premature replacement of equipment.
Increased safety for laboratory workers will result from well-maintained equipment.
A major part of equipment maintenance is PREVENTIVE maintenance

## Slide 39: Questions? Comments?
Organization
Personnel
Equipment
Purchasing & Inventory
Process Control
Information Management
Documents & Records
Occurrence Management
Assessment
Process Improvement
Customer Service
Facilities & Safety