## Slide 1
Process Control: Quality Control of Qualitative and Semi-Quantitative Procedures

## Slide 2: Learning Objectives
<number>
At the end of this module, participants should be able to:
Differentiate between built-in and traditional controls.
Describe how to use stock cultures for microbiology QC.
Discuss the use of quality control procedures for stains used in microscopic examination.
Describe methods for verifying performance of microbiological media.
Notes: <number>

## Slide 3: Scenario
Laboratory A performs a culture, and Pseudomonas aeruginosa is identified.
What QC measures can you use to confirm that the isolate is correctly identified?

## Slide 4: The Quality Management System
Organization
Personnel
Equipment
Purchasing & Inventory
Process Control
Information Management
Documents & Records
Occurrence Management
Assessment
Process Improvement
Customer Service
Facilities & Safety
Notes: <number>

## Slide 5: Qualitative or semi-quantitative tests - Examples
microscopic examinations
dipsticks
serologic procedures
microbiological procedures
any reaction that produces non-numeric results
<number>
Notes: <number>

## Slide 6: Important Concepts
sample management
staff competency
equipment maintenance
control materials
stains, media and reagents management
record keeping
<number>
Notes: <number>

## Slide 7: Quality Control Materials
built-in controls
control materials that mimic patient samples
reference organisms

## Slide 8: Built-in Controls
integrated into the design of a test kit device
automatically run with each test performed
assess certain aspects of kit performance
may not assess entire testing process

## Slide 9: Traditional Controls
materials with known reactivity
mimic patient samples
assess the integrity of the entire test system

## Slide 10: Using Traditional Controls
test as per patient samples
use a positive and negative control
include a weak positive control for immunological procedures
choose positive controls close to the cut-off value
include control to monitor extraction phase
<number>

## Slide 11: Stock Cultures for QC
<number>
reference strains
in-house developed strains
predictable reactions in stains and media
ensure media, reagents and supplies work as intended
Notes: <number>

## Slide 12: Sources for Obtaining Reference Strains
  ATCC-American Type Culture Collection
  NTCC-National Type Culture Collection (UK)
  CIP- Pasteur Institute Collection (France)
<number>

## Slide 13: Stains are important— take care of them!
<number>
No Attention
Continued Attention
Notes: <number>

## Slide 14: Stain Management
<number>
use established procedure for preparation or reconstitution
label: content, concentration, date prepared and placed in service, expiration, initials
store appropriately
Notes: <number>

## Slide 15: Quality Control for Stains
<number>
As appropriate for particular stain:
  check with known organisms or cells
  examine for crystal shards or for precipitation
  examine for contaminants such as bacteria and fungi
Left: Wright stain
Right: Gram stain
Notes: <number>

## Slide 16: Gram Stain
<number>
Good Quality
Poor Quality
Notes: <number>

## Slide 17: QC of Microbiology Media
<number>
verify performance of all media
in-house prepared: all batches
commercially prepared: new lot only
MacConkey Agar
QC
Left: non-lactose fermenter
Right: lactose fermenter
Notes: <number>

## Slide 18: Media Problems to Avoid
<number>
out-dated
dried-out
contaminated
Human blood should not be used because:
too much batch to batch variation
may include inhibitory substances, including antimicrobials
may contain biohazards (e.g., hepatitis virus)
Notes: <number>

## Slide 19: Quality Control of Growth Media
<number>
keep records for media prepared in-house
record outcomes in a dedicated media logbook for:
  pH, sterility, ability to support growth using stock cultures, biochemical response of stock cultures
frequency
  test each new batch or lot number
Notes: <number>

## Slide 20: Summary
<number>
  qualitative tests produce non-numerical results
  semi-quantitative tests give an estimate
  establish a QC program for qualitative and semi-quantitative tests
Notes: <number>

## Slide 21: Key Messages
QC procedures followed by ALL staff
always record QC results and corrective actions
If QC results are not acceptable, do not report patient results!
<number>

## Slide 22: Questions? Comments?
Organization
Personnel
Equipment
Purchasing & Inventory
Process Control
Information Management
Documents & Records
Occurrence Management
Assessment
Process Improvement
Customer Service
Facilities & Safety