## Slide 1: 08
Performing the SARS-CoV-2 Antigen RDT

## Slide 2: Disclaimer
WHO Health Security Learning Platform – Training Materials
These WHO Training Materials are © World Health Organization (WHO) 2022. All rights reserved.
Your use of these materials is subject to the “WHO Health Security Learning Platform, Training Materials – Terms of Use”, which you accepted when downloading them and which are available on the Health Security Learning Platform at: https://extranet.who.int/hslp.
Should you adapt, modify, translate, or in any other way revise the contents of these materials, you shall not imply that WHO is in any way affiliated with such modifications and shall not use the WHO name or emblem in such modified materials.
Furthermore, please inform WHO of any modifications of these materials that you use publicly, for record-keeping purposes and continued development, by emailing ihrhrt@who.int.

## Slide 3: Learning objectives
At the end of this module, you should be able to:
describe the key steps to follow to perform SARS-CoV-2 Antigen RDTs;
explain how to interpret individual test results.
This slide may need to be adapted based on the SARS-CoV-2 Antigen RDT in use

## Slide 4: SARS-CoV-2 Antigen RDT testing
The test procedures and interpretation of SARS-CoV-2 Antigen RDT results are similar for all tests.
It is important to follow the test-specific Instructions for Use, as reagents and procedures including incubation times may vary between different tests.

## Slide 5: SARS-CoV-2 Antigen RDT kit contents
Test device (individually wrapped in a foil pouch with desiccant)
Extraction buffer tube
Nozzle cap
Sterile swab
Paper stand
Instructions for Use
This slide may need to be adapted based on the SARS-CoV-2 Antigen RDT in use

## Slide 6: Precautions
Do not re-use the SARS-CoV-2 Antigen RDT kit components.
Do not use the SARS-CoV-2 Antigen RDT kit if the pouch is damaged, or the seal is broken.
Never use the extraction buffer tube from another lot of the same test or from different test brands.
This slide may need to be adapted based on the SARS-CoV-2 Antigen RDT in use

## Slide 7: Getting ready
Carefully read the SARS-CoV-2 Antigen RDT Instructions for Use.
Check the expiry date. Do not use the kit if the expiry date has passed. Kit materials are stable until the expiry date printed on the outer box.
Check that the test device and the desiccant pack are not damaged or invalid.
Store the SARS-CoV-2 Antigen RDT out of direct sunlight and at the temperature recommended by the manufacturer.
Do not freeze the kit.
Hand hygiene and wearing the recommended PPE while performing the testing is mandatory.
This slide may need to be adapted based on the SARS-CoV-2 Antigen RDT in use

## Slide 8: SARS-CoV-2 Antigen RDT testing procedure (1)
1. Insert the swab into an extraction buffer tube. While squeezing the buffer tube, stir the swab.
2. Remove the swab while squeezing the sides of the tube to extract the liquid from the swab.
3. Press the nozzle cap tightly onto the tube.
This slide may need to be adapted based on the SARS-CoV-2 Antigen RDT in use

## Slide 9: SARS-CoV-2 Antigen RDT testing procedure (2)
4. Apply drops of extracted specimen to the specimen well of the test device. Add the exact number of drops specified by the manufacturer.
5. Read and record the test result after the specified period of time.
This slide may need to be adapted based on the SARS-CoV-2 Antigen RDT in use

## Slide 10: SARS-CoV-2 Antigen RDT testing procedure (3)
6. Record the test result in the SARS-CoV-2 Antigen RDT Logbook.
7. Report the test result.
8. Dispose of all waste (used test kit, extraction buffer tube, swab and paper stand) in the biohazard bag.
9. Remove medical mask, gown, gloves, and eye protection or face-shield.
10. Perform hand hygiene.
This slide may need to be adapted based on the SARS-CoV-2 Antigen RDT in use

## Slide 11: Interpreting RDT results
RDT results should be considered together with the patient’s clinical history and other available information.
Interpreting the RDT result on the device:
A coloured band will appear in the top section of the result window to show that the test is working properly. This band is the control line (C).
A coloured band will appear in the lower section of the result window. This band is the test line for SARS-CoV-2 antigen (T).

## Slide 12: Result interpretation: Negative results
A line in “C” and NO LINE in “T” means SARS-CoV-2 is NOT DETECTED.
The test result should be interpreted as a NEGATIVE result.
NEGATIVE
This slide may need to be adapted based on the SARS-CoV-2 Antigen RDT in use

## Slide 13: Result interpretation: Positive results
A line in “C” AND a line in “T” means SARS-CoV-2 is DETECTED.
Even if the control line is faint or the test line isn't uniform, the test should be considered to have been performed properly and the test result should be interpreted as a POSITIVE result.
POSITIVE
This slide may need to be adapted based on the SARS-CoV-2 Antigen RDT in use

## Slide 14: Result interpretation: Invalid results
NO LINE in “C” and a line or no line in “T” means the test is INVALID.
Repeat the test using a new (unopened) SARS-CoV-2 Antigen RDT device and a new sample.
INVALID
This slide may need to be adapted based on the SARS-CoV-2 Antigen RDT in use

## Slide 15: Reading RDTs
This slide may need to be adapted based on the SARS-CoV-2 Antigen RDT in use

## Slide 16: Demonstration video
To play the video: https://www.youtube.com/watch?v=hED71QH1XRo

## Slide 17: Demonstration & practical

## Slide 18: Activity: Workstation setup
Instructions:
Identify your workstation in the practical room.
Gather test kits and supplies.
Obtain one POSITIVE and one NEGATIVE control sample from your instructor.
Arrange all items at your workstation.
Total time: 5 minutes

## Slide 19: Hands-on practice
Instructions:
Use safety precautions and wear personal protective equipment (PPE).
Perform two SARS-CoV-2 Antigen RDTs with the control samples provided by your instructor (if control samples are not available, testing may be performed on samples collected as part of the training session).
Raise your hand if you need additional supplies.
Document the SARS-CoV-2 Antigen RDT results.
Show your test results and test devices to your instructor after you are done.
Total time: 45 minutes

## Slide 20: Practical interpretation of test results

## Slide 21: Activity: Test interpretation (1)
Instructions:
Interpret the test results from the SARS-CoV-2 Antigen RDT Reading Sheet provided.
Record your results.
Raise your hand if you need help.
Total time: 5 minutes

## Slide 22: Activity: Test interpretation (2)
Answers:
Positive / NEGATIVE / invalid
Positive / negative / INVALID
POSITIVE / negative / invalid
POSITIVE / negative / invalid
Positive / NEGATIVE / invalid
Answers:
POSITIVE / negative / invalid
Positive / NEGATIVE / invalid
Positive / negative / INVALID
Positive / NEGATIVE / invalid
POSITIVE / negative / invalid
This slide may need to be adapted based on the SARS-CoV-2 Antigen RDT in use

## Slide 23: Common SARS-CoV-2 Antigen RDT challenges
Refer to SARS-CoV-2 Antigen Rapid Diagnostic Test − Frequently Asked Questions for more information on common SARS-CoV-2 Antigen RDT challenges and more information on SARS-CoV-2 Antigen RDT testing.

## Slide 24
Key points
Follow the instructions for use (IFU) of the test kit to perform the test.
Ensure that the kit is not damaged and in date before using it.
Record the results in the RDT logbook.
When interpreting the test results, always check that the control line is present. If not present, the result is invalid and the test should be repeated using a new RDT.

## Slide 25: Questions?