## Slide 1: 06
Sample collection

## Slide 2: Disclaimer
WHO Health Security Learning Platform – Training Materials
These WHO Training Materials are © World Health Organization (WHO) 2022. All rights reserved.
Your use of these materials is subject to the “WHO Health Security Learning Platform, Training Materials – Terms of Use”, which you accepted when downloading them and which are available on the Health Security Learning Platform at: https://extranet.who.int/hslp.
Should you adapt, modify, translate, or in any other way revise the contents of these materials, you shall not imply that WHO is in any way affiliated with such modifications and shall not use the WHO name or emblem in such modified materials.
Furthermore, please inform WHO of any modifications of these materials that you use publicly, for record-keeping purposes and continued development, by emailing ihrhrt@who.int.

## Slide 3: Learning objectives
At the end of this module, you should be able to:
describe the personal protective equipment (PPE) required for sample collection;
explain how to prepare your sample collection workstation/area;
describe what samples are recommended for SARS-CoV-2 testing;
describe the precautions to take when collecting samples for SARS-CoV-2 testing;
describe how to package samples for transport.

## Slide 4: Introduction to sample collection
Proper sample collection is critical in the laboratory diagnosis of COVID-19.
The result of any diagnostic test is only as good as the sample received.
A sample that is not collected correctly may lead to a false-negative test result and could result in someone with COVID-19 potentially not isolating or not receiving the appropriate care.
Nasopharyngeal swabs are often the preferred sample for testing using SARS-CoV-2 Antigen RDTs. Other sample types are also being used, such as nasal and throat swabs (often for self-testing kits). Always refer to the kit’s IFU which will specify the type of samples to use.

## Slide 5: Sample collection workstation1
Collect samples for SARS-CoV-2 testing wearing the appropriate PPE (described later in this module).
Ensure that all supplies are available before performing the sample collection.
Collect the sample in a normal procedure room with the door closed.
Limit the number of healthcare workers present during the procedure to only those essential for patient care and procedure support.
Others not involved in the procedure, including visitors, should not be present for sample collection.
1 The workstation setup may need to be revised if sample collection takes place in the field.

## Slide 6: Supplies and materials
New (unopened) individually wrapped sterile nasopharyngeal swab
Primary receptacle (e.g., viral transport media or tube with buffer)
PPE, including gloves, gown, eye protection; goggles or face-shield, and medical mask 2
Pen for marking or labelling
Bleach, ethanol and paper towels to clean the workstation
Sample collection form
Soap for hand-washing or alcohol-based hand rub
Leak-proof biohazard bags and waste bins for containing or moving biohazard waste
1 As new tests becomes available, other sample types may be used.
2 Respirators are recommended for settings where aerosols generating procedures are performed. Based on values and preferences and if widely available, they could also be used when providing direct care to COVID-19 patients in other settings.
Adapt according to the guidelines in your country

## Slide 7: What PPE is recommended for the health care worker during sample collection?
Long-sleeved isolation gown on top of scrub suits, which fully cover your torso and extend from your neck to your knees, and cover your arms to the end of your wrists
A medical mask that is secured properly and fits your face
Eye protection (e.g., goggles or disposable full face-shield) that can be adjusted to fit your face and cover your eyes, nose, mouth and chin
Clean, non-sterile, disposable gloves that cover the wrist area of your isolation gown

## Slide 8: Sample collection: General guidelines (1)
Read, understand and adhere strictly to all applicable biosafety measures for collecting, handling and managing samples for SARS-CoV-2 testing.
Collect the sample as soon as possible once a decision has been made to pursue SARS-CoV-2 testing, regardless of the time of symptom onset.
Adhere strictly to established sample collection procedures to obtain high-quality samples.
Adapt according to the guidelines in your country

## Slide 9: Sample collection: General guidelines (2)
Clean and disinfect the procedure room surfaces promptly before and after sample collection using appropriate disinfectants and the recommended contact time for the specific disinfectant.
Label each sample with the patient’s unique identification (ID) number (e.g., medical record number), unique sample ID (e.g., laboratory requisition number), sample type, and the date and time the sample was collected.
Strictly adhere to recommended hand hygiene and biosafety measures.
Adapt according to the guidelines in your country

## Slide 10: Sample collection: General guidelines (3)
Testing should be performed immediately after sample collection.
Use only the materials and reagents (e.g., extraction buffer) the manufacturer supplied with the test.
If testing cannot be performed immediately after sample collection, follow the manufacturer’s recommendations for storage.
According to your country algorithm, if a second sample is to be collected for NAAT molecular testing, ensure that appropriate materials and reagents (e.g., viral transport media) are available at the workstation.
Adapt according to the guidelines in your country

## Slide 11: Collecting a nasopharyngeal swab (1)
Insert a sterile nasopharyngeal swab into the nasal cavity of the patient, reaching the surface of the posterior nasopharynx.
Swab over the surface of the posterior nasopharynx, rotating the swab 3−4 times to ensure a good sample. Leaving the swab in the nasal cavity for a few seconds will ensure absorption of the nasal secretions.
Withdraw the sterile swab from the nasal cavity.

## Slide 12: Collecting a nasopharyngeal swab (2)
If collection from one nostril is not successful, collect a sample from the other nostril with the same swab.
After collecting the sample, perform the SARS-CoV-2 Antigen RDT according to the manufacturer’s instructions (see Module 08: Performing the SARS-CoV-2 Antigen RDT).
When placing swabs in a tube, if swabs do not have breaking point, promptly disinfect the scissors used to cut the swab before and after cutting the swab.
If a second sample is to be collected for NAAT molecular testing according to your country’s testing algorithm, do so immediately after collecting the sample for SARS-CoV-2 Antigen RDT testing.

## Slide 13: Collecting a nasopharyngeal swab (video)
To play the video: How to collect oropharyngeal and nasopharyngeal specimens for the diagnosis of COVID-19

## Slide 14: Transporting samples to the laboratory

## Slide 15: Things to consider when packaging samples for transport1,2
Be aware. There is a risk of exposing people or the environment to the samples during transport.
Take care. Samples for SARS-CoV-2 testing must be triple packaged. Triple packaging protects the sample from breaking or leaking in transit and prevents contamination of the courier and the environment if breakage/leakage does occur.
Be proactive. If you don’t have commercial triple packages available, you can improvise from common items found at your facility if they adhere to the triple packaging principles (explained on the next slide). Sample transportation within institution can be done using a plastic box with covers or tablet.
1 Guidance on regulations for the transport of infectious substances 2021–2022. Geneva: World Health Organization; 2021 (https://www.who.int/publications/i/item/9789240019720, accessed 13 April 2021).
2 Guidance for use of pneumatic tube systems for transport of respiratory specimens from suspected or confirmed COVID-19 patients. Atlanta: Centers for Disease Control and Prevention; 2020 (https://www.cdc.gov/csels/dls/locs/2020/transport_recommendations_for_covid-19_specimens.html,accessed 28 October 2020).

## Slide 16: Examples of triple packaging for SARS-CoV-2 samples1
The three layers that constitute triple packaging include the primary receptacle, secondary packaging and outer packaging.
The outer packaging is made from an ice chest with lid and protects the secondary packaging, which is made from watertight material.
The primary receptacle is placed in the secondary packaging and includes additional absorbent and cushioning material.
Source : Laboratory biosafety manual. 4th edition. Geneva: World Health Organization; 2021
1 If you ship samples to World Health Organization reference laboratories or collaborating centres outside the country or ship samples by air, you must ensure compliance with the Recommendations on the Transport of Dangerous Goods—Model Regulations (22nd revised edition, United Nations) and the Technical Instructions for the Safe Transport of Dangerous Goods by Air (ICAO).
Guidance on regulations for the transport of infectious substances 2021–2022. Geneva: World Health Organization; 2021

## Slide 17
Key points (1)
Proper sample collection is critical in the laboratory diagnosis of COVID-19.
Wear appropriate PPE which should include respiratory protection; ie a medical mask, eye protection, gown, disposable gloves.
Collect samples as early as possible after the decision to test has been made.

## Slide 18
Key points (2)
Testing should be performed immediately after specimen collection.
When it is required to store and/or send the samples prior to testing, follow the appropriate procedures. Samples should notably be packaged using a triple packaging system.

## Slide 19: Questions?