## Slide 1: 05
Safety for SARS-CoV-2 Antigen RDT testing

## Slide 2: Disclaimer
WHO Health Security Learning Platform – Training Materials
These WHO Training Materials are © World Health Organization (WHO) 2022. All rights reserved.
Your use of these materials is subject to the “WHO Health Security Learning Platform, Training Materials – Terms of Use”, which you accepted when downloading them and which are available on the Health Security Learning Platform at: https://extranet.who.int/hslp.
Should you adapt, modify, translate, or in any other way revise the contents of these materials, you shall not imply that WHO is in any way affiliated with such modifications and shall not use the WHO name or emblem in such modified materials.
Furthermore, please inform WHO of any modifications of these materials that you use publicly, for record-keeping purposes and continued development, by emailing ihrhrt@who.int.

## Slide 3: Learning objectives
At the end of this module, you should be able to:
  describe what personal protective equipment (PPE) is needed and how to use it;
  explain how to prepare and use disinfectants;
  explain how to safely perform tests and safely dispose of waste.
Notes: I would change it to …, you will: know ….

## Slide 4: SARS-CoV-2 transmission (1)
SARS-CoV-2 spreads between people through direct, indirect (through contaminated objects or surfaces) or close contact with infected people via mouth and nose secretions that are released when an infected person coughs, sneezes, speaks, breathes or sings.
People who are in close contact with an infected person can catch SARS-CoV-2 when those infectious droplets get into their mouth, nose or eyes.

## Slide 5: SARS-CoV-2 transmission (2)
To avoid contact, it is important to stay at least 1 meter away from others, clean hands frequently, and cover the mouth with a tissue or bent elbow when sneezing or coughing.
When physical distancing (standing 1 meter or more away) is not possible, wearing a mask is an important measure to protect others. Cleaning hands frequently is also critical.

## Slide 6: SARS-CoV-2 transmission (3)
Sample collection can produce very small droplets that are able to stay suspended in the air for longer periods of time.
  This procedure is not considered an aerosol generating procedure (AGP) 1
When collecting samples from people infected with SARS-CoV-2, these droplets can contain SARS-CoV-2.
These droplets may potentially be inhaled by healthcare workers or others if they are not wearing appropriate personal protective equipment (PPE). Wearing the correct PPE for the procedure will ensure there is a low risk of transmission
Others not involved in the procedure should not be permitted in areas where sample collection is being performed.
1 Infection prevention and control during health care when coronavirus disease (COVID-19) is suspected or confirmed. Interim guidance, 12 July 2021. Geneva: World Health Organization; 2021

## Slide 7: Conducting a biological risk assessment (1)
A biological risk assessment is a systematic process of gathering information and evaluating the likelihood and consequences of exposure to or release of workplace hazard(s) and determining the appropriate risk control measures to reduce the risk.
STEP 1. Gather information (hazard identification)
STEP 2. Evaluate the risks
STEP 3. Develop a risk control strategy
STEP 4. Select and implement risk control measures
STEP 5. Review risks and risk control measures

## Slide 8: Conducting a biological risk assessment (2)
Risk assessment should be a continuous process.
It should be performed at the beginning of all work containing biological agents and whenever changes take place in the following:
  personnel
  facility
  equipment
  methods
  regulations.
For more information on conducting risk assessments see: Risk assessment and management of exposure of health care workers in the context of COVID-19: Interim guidance, 19March 2020, and 9 September 2020 and Laboratory biosafety guidance related to coronavirus disease (COVID-19): Interim guidance, 28 January 2021

## Slide 9: Risk level for SARS-CoV-2 Antigen RDT procedures
Procedure | Initial risk * | Residual risk **
Sample collection | Medium to high | Low to medium
Sample receipt and accession | Low | Low
SARS-CoV-2 Antigen RDT testing | Low | Low
* Initial risk: Risk prior to any specific precautions being in place (e.g., ventilation, PPE)
** Residual risk: Risk remaining after basic precautions are in place (e.g., ventilation, PPE)

## Slide 10: What you should do before sample collection and testing
Put on appropriate PPE
Procedure | PPE
Sample collection | Non-sterile gloves; single-use only Gown1 Eye protection (safety glasses or goggles, face-shields [visors]) Medical mask 2,3
Sample receipt and accession | Non-sterile gloves; single-use only Gown Eye protection (safety glasses or goggles, face-shields [visors]) Medical mask3
SARS-CoV-2 Antigen RDT sample testing | 
1 Solid front or wrap-around gowns, scrub suits, or coveralls with sleeves that fully cover the forearms; head coverings; and shoe covers or dedicated shoes
2 Advice on the use of masks in the context of COVID-19 Interim guidance, 23 December 2020; Rational use of personal protective equipment for COVID-19 and considerations during severe shortages. Geneva: World Health Organization; 2020, Infection prevention and control during health care when coronavirus disease (‎COVID-19)‎ is suspected or confirmed. Interim guidance, 12 July 2021
Respirators are recommended for settings where aerosols generating procedures are performed. Based on values and preferences and if widely available, they could also be used when providing direct care to COVID-19 patients in other settings.
3 Medical masks are defined as surgical or procedure masks that are flat or pleated; they are affixed to the head with straps that go around the ears or head or both. Their performance characteristics are tested according to a set of standardized test methods (ASTM F2100, EN 14683, or equivalent) that aim to balance high filtration, adequate breathability and, optionally, fluid penetration resistance.
Adapt according to the guidelines in your country

## Slide 11: How to put on and how to take off PPE
Course available on: https://openwho.org/courses/IPC-PPE-EN (COVID-19: How to put on and remove personal protective equipment (PPE))
Other resources: WHO biosafety video series: https://www.who.int/ihr/publications/biosafety-video-series/en/
Play the video by clicking here

## Slide 12: Setting up the workstation
SARS-CoV-2 Antigen RDT testing must be performed on a designated well-ventilated bench, separate from the sample collection area and other areas where patients have access.
The work area should be marked with a biohazard sign and accessible only to staff who have been trained, are conducting the testing and are wearing appropriate PPE.
Adapt according to the guidelines in your country

## Slide 13: Workstation setup
Supplies
Testing done here
(place a diaper or similar absorbent material)
SARS-CoV-2 Antigen RDT Logbook
SARS-CoV-2 Ag RDT
Timer
Gloves
Waste container and disinfectants
(0.1% and 0.5% Bleach
& 70% Ethanol)

## Slide 14: When working with SARS-CoV-2 Antigen RDTs, you should:
Change gowns and gloves if they become soiled or contaminated.
Remove gowns and gloves before leaving the work area and between testing samples.
Discard disposable gowns after single use. Cloth gowns should be re-used following proper cleaning and decontamination.
Always perform hand hygiene before and after working with samples and before and after using gloves.
Adapt according to the guidelines in your country

## Slide 15: Disinfectants

## Slide 16: Disinfectants for SARS-CoV-2
Not all disinfectants are effective against SARS-CoV-2.
Bleach and ethanol are two commonly available disinfectants active against SARS-CoV-2.
Follow national guidelines or international guidance when selecting disinfectants.1
Type | Working Concentration2 | Comments
Sodium hypochlorite (bleach3) | 0.1% | A general-purpose disinfectant that can be used for general surface disinfection
Sodium hypochlorite (bleach3) | 0.5% | A general-purpose disinfectant that can be used to soak items and disinfect spills. Corrosive to metals and plastics
Ethanol | 70% | Leaves no residue. Use with other disinfectants to decontaminate surfaces (including metals)
1 Laboratory biosafety manual. 4th edition. Geneva: World Health Organization; 2021 (https://www.who.int/publications/i/item/9789240011311).
2 Concentration refers to the strength of the disinfectant.
3 Household bleach varies in concentration between 3% and 5%. Do not use bleach when working with products containing guanidinium iso/thiocyanate (GITC/GTC). In that case, you may use a 70% solution of ethanol or isopropyl alcohol. Verify manufacturers’ instructions for use.
Adapt according to the guidelines in your country

## Slide 17: Preparation and use of disinfectants
Disinfect the workstation before and after use and immediately after a spill occurs.
Contact time, dilution and shelf life of the working disinfectant solution (after dilution) are all critical for effective disinfection.
Always leave disinfectants in contact with surfaces or spills for the recommended time, usually 10–15 minutes.
Prepare working solution of sodium hypochlorite (bleach) daily by diluting from the concentrated disinfectant solution, as diluted sodium hypochlorite degrades rapidly losing efficacy.
Mark the date of dilution on the bottle and only use on the day of preparation.
Do not use bleach when working with products containing guanidinium iso/thiocyanate (GITC/GTC). In that case, you may use a 70% solution of ethanol or isopropyl alcohol. Verify manufacturers’ instructions for use.
Adapt according to the guidelines in your country

## Slide 18: Diluting disinfectants: Bleach – example of a 0.5% solution
To make a 0.5% sodium hypochlorite (bleach) solution from household bleach (5% sodium hypochlorite):
In a suitable container or spray bottle, add 10ml of household bleach to 90ml of water.
Label the container or spray bottle with the name of the disinfectant (0.5% bleach), the date of preparation and the initials of the staff who prepared the solution.
Prepare the diluted bleach disinfectant daily and discard any unused disinfectant at the end of the day.
Only use the disinfectant on the day of preparation.
Adjust the dilution based on the starting concentration of the household bleach (usually between 3% and 5%).

## Slide 19: Diluting disinfectants: Ethanol
To make a 70% ethanol solution from 100% ethanol:
In a suitable container or spray bottle, add 70ml of 100% ethanol to 30ml of water.
Label the container or spray bottle with the name of the disinfectant (70% ethanol) and the date of preparation.
Ethanol may be stored in a container or spray bottle.

## Slide 20: Managing a spill
Wearing gloves and a gown:
Cover the spill area with 0.5% bleach.
Cover the spill and disinfectant with paper towel.
Leave for at least 10 minutes.
Wipe up the spill and disinfectant with paper towel and discard in the biohazard waste container.
Disinfect the area with 0.5% bleach and dry with paper towel. Discard the paper towel in the biohazard waste container.
Disinfect the area with 70% alcohol and dry with paper towel. Discard the paper towel in the biohazard waste container.
Do not use bleach when working with products containing guanidinium iso/thiocyanate (GITC/GTC). In that case, you may use a 70% solution of ethanol or isopropyl alcohol.

## Slide 21: Waste management

## Slide 22: Managing waste (1)
Handle all waste from sample collection (eg. sample container, if different from extraction tube) and disposable PPE as biohazardous. Autoclave or incinerate infectious waste.1
1 Laboratory biosafety manual. 4th edition. Geneva: World Health Organization; 2021 (https://www.who.int/publications/i/item/9789240011311).

## Slide 23: Managing waste (2)
Disposal of SARS-CoV-2 Antigen RDT used cassettes, used extraction tubes (and other consumables such as transfer pipettes):
  Read the kit’s manufacturers’ specific instructions.
    Note: Some antigen RDT kits’ extraction buffers, when used according to the IFU, will inactivate SARS-CoV-2 virus when the sample is added to the buffer in the extraction tube. Indicated waste management procedures may be found in the IFU.
  Read Material Safety Data Sheets.
    Note: antigen RDT kit extraction’s buffer may contain sodium azide and autoclaving should be avoided when handling large volumes of sodium azide. Accumulation of sodium azide in contact with metal may result in a serious hazard with heat or shock.
  Follow national, local regulations for disposal.
  In the absence of otherwise recommendations from national authorities or the manufacturer, handle SARS-CoV-2 Antigen RDT as biohazardous.

## Slide 24: What you should do after testing
All components of SARS-CoV-2 Antigen RDTs are single-use and must not be reused.
Place all potentially contaminated materials (such as used sample containers, used extraction tubes, transfer pipettes and used test cassettes) in a biohazard bag.
At the end of the day, seal the biohazard bag, and follow your facility’s guidelines for biohazardous waste disposal.
Adapt according to the guidelines in your country

## Slide 25: Testing in the community
Take enough biohazard bags when going to perform testing in the community.
Place all potentially contaminated materials (such as used sample extraction tubes, transfer pipettes and used test cassettes) in a biohazard bag and seal the bag.
Use a new (unused) biohazard bag for waste disposal at different locations in the community.
Return the sealed biohazard bags to the health facility for autoclaving1 or incineration.
    1 SARS-CoV-2 Antigen RDT kit extraction’s buffer may contain sodium azide – autoclaving should be avoiding when handling large volumes of sodium azide. Accumulation of sodium azide in contact with metal may result in a serious hazard with heat or shock.
Adapt according to the guidelines in your country

## Slide 26
Key points (1)
Wear appropriate PPE which should include respiratory protection, eye protection, gown, and gloves.
The type of PPE to be used may be adapted based on a local risk assessment.
Testing should be done in a separate well-ventilated room.

## Slide 27
Key points (2)
Bleach (sodium hypochlorite) and ethanol are both active against SARS-CoV-2.
Contact time, dilution and shelf life of the working disinfectant solution (after dilution) are all critical for effective disinfection.
Handle all waste from sample collection and SARS-CoV-2 Antigen RDT testing as biohazardous unless indicated otherwise.

## Slide 28: Questions?