## Slide 1: 09
Using SARS-CoV-2 RDT data

## Slide 2: Disclaimer
WHO Health Security Learning Platform – Training Materials
These WHO Training Materials are © World Health Organization (WHO) 2022. All rights reserved.
Your use of these materials is subject to the “WHO Health Security Learning Platform, Training Materials – Terms of Use”, which you accepted when downloading them and which are available on the Health Security Learning Platform at: https://extranet.who.int/hslp.
Should you adapt, modify, translate, or in any other way revise the contents of these materials, you shall not imply that WHO is in any way affiliated with such modifications and shall not use the WHO name or emblem in such modified materials.
Furthermore, please inform WHO of any modifications of these materials that you use publicly, for record-keeping purposes and continued development, by emailing ihrhrt@who.int.

## Slide 3: Learning objectives
At the end of this module, you should be able to:
list what documents and records should be available at the testing site;
describe the contents of the SARS-CoV-2 Antigen RDT logbook and how to use it;
describe the purpose of quality indicators;
list the quality indicators to be monitored for SARS-CoV-2 Antigen RDTs;
explain how to analyze SARS-CoV-2 Antigen RDT data.

## Slide 4: Record keeping

## Slide 5: Record keeping
Record keeping allows the testing site to:
monitor the quality of testing
track the number of tests performed
determine the supplies needed for testing.

## Slide 6: Documents and records for RDTs
Documents
  Include written policies, process descriptions and standard operating procedures (SOPs)
  Are used to communicate information about testing policies and procedures
Records
  Consist of information captured on worksheets, forms and charts
  Are used to record data about testing procedures and results

## Slide 7: What documents should you keep onsite?
Country policies and testing algorithm
Safety manuals
SOPs including:
  Preparing disinfectant
  Sample collection
  Testing procedures
  Waste management
Performing quality control (QC)
Performing External Quality Assessment (EQA)
Adapt according to the guidelines in your country

## Slide 8: What records should you keep onsite?
Test requisition forms
Specimen transfer logs
SARS-CoV-2 Antigen RDT Logbook
Temperature logs (e.g., temperature-sensitive equipment, cold storage)
Inventory records
COVID-19 surveillance register
Post-market surveillance user feedback form here
Adapt according to the guidelines in your country

## Slide 9: Tips for good record keeping
Understand the information that is being recorded.
Ensure that all information is recorded every time a procedure is performed.
Ensure that all critical information is recorded:
  patient information
  test kit name, lot number, expiry date
  individual and final test results.
The information should be documented the same way every time.

## Slide 10: SARS-CoV-2 Antigen RDT Logbook *
  The SARS-CoV-2 Antigen RDT Logbook:
  serves as an ongoing quality assurance tool
  identifies problems
  helps identify how many tests have been performed
  provides data for quality indicator (QI) monitoring
* A template is available as part of this SARS-CoV-2 Antigen Rapid Diagnostic Test training package
https://extranet.who.int/hslp/content/sars-cov-2-antigen-rapid-diagnostic-test-training-package

## Slide 11: SARS-CoV-2 Antigen RDT Logbook
1
2
3
4
5
6
  The SARS-CoV-2 Antigen RDT Logbook records the following information:
  Sample identification number, patient age, sex, etc.
  Test kit name, lot number and expiry date
  SARS-CoV-2 Antigen RDT, NAAT and final test results
  Who performed the test
  Page totals summarized when completed
  Supervisor signature at bottom of page to verify Logbook
5
5
3
3
5

## Slide 12: Storing documents and records
Ensure that documents and records are kept in a safe place and are easily retrievable.
Ensure complete confidentiality of patients’ records by properly storing records that contain COVID-19-related information:
  Keep records out of view of other patients and staff.
  Keep records in a locked cabinet when not in use.

## Slide 13: Collecting quality indicators

## Slide 14: What are quality indicators (QIs)?
QIs, also known as key performance indicators, are objective measures of how well a diagnostic test is working.
As it is not feasible to monitor the performance of every step of the testing process, QIs help you to identify issues early on that may impact the quality of test results, and to take actions to correct the errors (corrective action) and reduce the chance of them re-occurring (preventive action).
QIs are obtained from documents and records, including the sample requisition form and the SARS-CoV-2 Antigen RDT Logbook.

## Slide 15: Why are QIs important?
Monitoring QIs is an essential component of all COVID-19 testing.
QIs are especially important in the context of the COVID-19 response, where there is strong pressure to rapidly scale up testing and provide results in time in order to inform decisions on patient management and public health responses, such as isolation and quarantine.
Tracking of QIs allow for the early identification of errors and other problems (e.g., delayed reporting of results) that can be resolved through investigation, and corrective and preventive actions.
Routine collection and analysis of QIs can assist in the planning and implementation of testing operations, and act as an integral part also contributing to post market surveillance

## Slide 16: Which QIs should be used to monitor COVID-19 testing?
The following QIs are collected from the daily and then weekly totals captured in the SARS-CoV-2 Antigen RDT Logbook (or equivalent):
Number and proportion of specimens tested, by specimen type, by batch/lot, by tester
Number and proportion of positive, negative and unsuccessful (invalid) SARS-CoV-2 Antigen RDT results
Number and proportion of COVID-19 patients positive by NAAT
Number of days where testing services have been interrupted
Number and proportion of spoilt tests (damaged packages, etc.)
Average turnaround time (from sample collection to reporting)
Adapt according to the guidelines in your country

## Slide 17: Collecting and analysing QI data (1)
Record daily and then weekly QI totals captured in the SARS-CoV-2 Antigen RDT Logbook.
Collate the totals across the testing site. Review for trends and compare to pre-determined targets.
Adapt according to the guidelines in your country

## Slide 18: Collecting and analysing QI data (2)
A great way to see QI data trends is to show the data points on a graph.
On a graph, plot various QIs and look for trends or outliers, such as:
  change in testing volume
  change in positivity rate
  increases in invalid test results
  testing delays.
Adapt according to the guidelines in your country

## Slide 19: Correcting the errors
Conduct further investigation to determine the reason (root cause) of QIs that fall outside of an acceptable range or have unusual trends. This may be done during supervisory visits.
Sites should seek help from supervisors if there are difficulties in identifying problems and corrective actions.
Breaking down errors by tester or batch may help to identify root causes due to operator error (e.g., errors occurring with new or untrained staff) or batch issues.
Undertake and document actions to correct errors and note what measures are put in place to prevent them from re-occurring (preventive actions).
Monitor the effectiveness of actions in terms of improving QIs.
Track the QI data over time (monthly and quarterly) for longer term trends that may not be apparent from weekly reports.
Adapt according to the guidelines in your country

## Slide 20: Example of how to correct errors
Example: Increased rate of invalid results
QI - Target invalid rate | <1%
Recorded invalid rate | 4%
Action | Review for any patterns and determine the reason. Determine which batch of RDTs had the issue − Is this a new batch? Determine which staff were performing the testing − Are they new staff? Have they received training? Determine if issues are related to sample collection. Establish the appropriate action to correct the issue and how to measure the success of the action. Implement the action. Monitor the effectiveness of the action − Did it address the error? Document and record all steps. Provide feedback to all staff in a weekly meeting.
Adapt according to the guidelines in your country

## Slide 21: Communicating issues promptly with the clinical team
When QIs fall outside of an acceptable/expected range, it is important to notify clinicians immediately.
Regular communication between the clinicians and testers is essential for managing the situation and delivering the best service possible to patients, given the importance of accurate and timely results for clinical decisions such as isolation and public health measures.
Adapt according to the guidelines in your country

## Slide 22: Communicating issues promptly with the manufacturer
Analysis of QI may indicate issues inherent to the test itself, in which case it should be immediately reported
Use of IVD user feedback form here
Post-market information on IVDs empowers national regulatory authorities and WHO to detect, investigate, communicate and contain events that threaten public health security and to take appropriate action
Regular communication between the testers and manufacturer is essential for managing the situation and delivering the best service possible to patients

## Slide 23: Reporting data to national or supervisory level (1)
QI data should be analysed and used for improving quality and patient management at the testing site.
However, it is equally important to regularly report the data to the national or supervisory level.
Certain trends (e.g., shortages of testing supplies) may require intervention from a higher level of the health system, or the testing site may need assistance to implement corrective actions.
Adapt according to the guidelines in your country

## Slide 24: Reporting data to national or supervisory level (2)
Collection of reports from different testing sites and analysis of data are useful for identifying trends that extend beyond individual laboratories (for example, national or regional shortages of testing supplies, or high invalid rates experienced with a single batch of RDTs).
Feedback resulting from this analysis should be provided to testing sites so that they may put in place measures to address the findings.
A list of available tools for reporting data to the national or supervisory level can be found at https://www.cdc.gov/coronavirus/2019-ncov/global-covid-19/compare-digital-tools.html.
Adapt according to the guidelines in your country

## Slide 25
Key points (1)
QIs are objective measures of how well a diagnostic test is working.
Tracking of QIs and following their trend allow for the early identification of errors and other problems (e.g., delayed reporting of results).
Identifying the reason for these errors and problems is key to implementing corrective measures and preventive actions.

## Slide 26
Key points (2)
Good documentation of the processes and good record keeping is essential to facilitate and monitor quality testing.
Documents describes policies and processes. Those include manuals and SOPs.
Records capture information on worksheets or forms. Those include may include the test requisition form, results logbook, other logbooks (eg. temperature monitoring, inventory).

## Slide 27: Questions?