## Slide 1
1
3.2.S.3.2 Impurities,
Malaysia, 29 September 2011
Impurities
Dr Antony Fake
WHO Prequalification Team - Medicines

## Slide 2: Introduction
This presentation is made with reference to the preparation of the API.
This is because the API is the source of the majority of impurities.
When considering FPPs, the focus is largely on degradants, although excipient-API and leaching from containers must not be overlooked.

## Slide 3: What kinds of impurities are there?
Things we add during preparation:

## Slide 4: What kinds of impurities are there?
Things we add during preparation:
  Solvents, metal catalysts, starting materials, reagents

## Slide 5: What kinds of impurities are there?
Things we add during preparation:
  Solvents, metal catalysts, starting materials, reagents
Things we unintentionally add during preparation:

## Slide 6: What kinds of impurities are there?
Things we add during preparation:
  Solvents, metal catalysts, starting materials, reagents
Things we unintentionally add during preparation:
  Starting materials impurities; impurities within solvents, pesticides...

## Slide 7: What kinds of impurities are there?
Things we add during preparation:
  Solvents, metal catalysts, starting materials, reagents
Things we unintentionally add during preparation:
  Starting materials impurities; impurities within solvents, pesticides...
Unwanted things that are made during preparation:

## Slide 8: What kinds of impurities are there?
Things we add during preparation:
  Solvents, metal catalysts, starting materials, reagents
Things we unintentionally add during preparation:
  Starting materials impurities; impurities within solvents, pesticides...
Unwanted things that are made during preparation:
  Reaction intermediates, related-substances

## Slide 9: What kinds of impurities are there?
Things we add during preparation:
  Solvents, metal catalysts, starting materials, reagents
Things we unintentionally add during preparation:
  Starting materials impurities; impurities within solvents, pesticides...
Unwanted things that are made during preparation:
  Reaction intermediates, related-substances
Things that are formed after preparation:

## Slide 10: What kinds of impurities are there?
Things we add during preparation:
  Solvents, metal catalysts, starting materials, reagents
Things we unintentionally add during preparation:
  Starting materials impurities; impurities within solvents, pesticides...
Unwanted things that are made during preparation:
  Reaction intermediates, related-substances
Things that are formed after preparation:
  Degradation products

## Slide 11: What are the potential impurities?
API SM
Reaction
intermediate
Final API
Reagents
Solvents
Catalysts
Degradation
By-products
By-products
SM
impurities
Reagents
Solvents
Catalysts
Potential Impurities
Residue of the SM
Residue of the intermediate
Impurities in the SM
Reagents
Solvents
Catalysts
Reaction by-products
Degradation products

## Slide 12: Where do we find information on impurities?
Things we add during preparation:
  Solvents, metal catalysts – 3.2.S.2.2
Things we unintentionally add during preparation:
  SM impurities; impurities within solvents, pesticides - 3.2.S.2.3
Unwanted things that are made during preparation:
  Reaction intermediates (3.2.S.2.3), related-substances (3.2.S.3.2)
Things that are formed after preparation:
  Degradation products (3.2.S.7)
  And of course 3.2.S.3.2 – Discussion of impurities

## Slide 13: Types of Impurities
Organic impurities
  Related substances and Degradation products
Solvents
Metals
Genotoxins

## Slide 14: API Monographs
You can not rely upon an API monograph entirely for potential organic impurities.
Many impurities are specific to the manner of API preparation and may not have been considered when the monograph was published.
Of course monographs are a great start.

## Slide 15: Potential Organic Impurities
The applicant should consider all potential impurities and then by logic, or by testing, reduce the set of potential impurities to a set of probable impurities.
There are probably four categories:
  Degradants
  Synthetic by-products of the API
  Remnants of earlier intermediates
  Synthetic by products of earlier intermediates

## Slide 16: Degradants
Degradants:
Forced degradation studies will provide information on major degradants.
Forced degradation studies will provide information on the acceptability of the analytical technique
Monographs tend to be better at listing degradants.

## Slide 17: Related Substances
Impurities are more difficult to predict.
Test method sensitivity is extremely important. What can it detect?
Mass balance should be kept in mind.
If there are multiple pharmacopoeial monographs, then at the very least consider all of these impurities. At least for investigation purposes.

## Slide 18
Setting specifications

## Slide 19: Thresholds and limits
Thresholds
The ICH reporting, identification, and qualification thresholds indicate levels at which the applicant is expected to undertake increasing control of an impurity.
Limits
In contrast an impurity limit is the non-negotiable allowable level for an impurity in a batch.

## Slide 20: Thresholds
QF Threshold
ID Threshold
Reporting
Threshold

## Slide 21: This is a limit
In contrast an impurity limit is the non-negotiable allowable level for an impurity in a batch.

## Slide 22: Reporting threshold
For APIs taken less then 2g per day
0.05%
For APIs taken greater then 2g per day
0.03%

## Slide 23: Exceeding the Reporting threshold
QF Threshold
ID Threshold
Reporting
Threshold

## Slide 24: Reporting threshold
Every time a peak is observed above the reporting threshold it needs to be recorded in the laboratory results.
It prevents the applicant from having to report every little peak that is observed in the chromatogram.
A peak above the reporting threshold does not (necessarily) need to be specified in the API specifications.
However, any peak above the reporting threshold must be counted towards the Total impurity content reported in the Certificate of Analysis.

## Slide 25: Identification threshold
For APIs taken less then 2g per day
The lesser of 0.10% or 1.0 mg TDI
For APIs taken greater then 2g per day
0.05%

## Slide 26: Exceeding the ID threshold
QF Threshold
ID Threshold
Reporting
Threshold

## Slide 27: Exceeding the ID threshold
If a peak is observed routinely above the ID threshold then the impurity must be:
Specified individually in the API specifications (by name or RRT).
Identified (or efforts made to do so)

## Slide 28: “Routinely Observed”
Normally, the decision to include an impurity in the specifications is based upon the likelihood it will occur routinely.
  For instance, observed above the ID threshold in long-term stability data, or commonly occurs in batches when tested at release.
An impurity only occurring in accelerated stability trials, forced degradation trials, or during development may not need to be included.

## Slide 29: Qualification threshold
For APIs taken less then 2g per day
The lesser of 0.15% or 1.0 mg TDI
For APIs taken greater then 2g per day
0.05%
An impurity limit above the Qualification threshold must be known to be safe.

## Slide 30: Exceeding the QF thresholds
QF Threshold
ID Threshold
Reporting
Threshold

## Slide 31: Justifying a limit exceeding the Qualification Threshold
Refer to a limit in a recognised monograph-
  WARNING – it must be a specified Impurity.
  …Impurity A , no more than 0.25% - OK
  …Any impurity no more than 0.5% - Not OK
Present literature evidence in support of the limit.
Present the results of toxicological studies supporting the safety of the limit.
Set the limit to 0.15% (or 1 mg TDI) and modify the process to meet this limit.

## Slide 32
The lesser of 0.15% or 1.0 mg TDI

## Slide 33: Example 1
A peak is observed at 0.086%.
Is this above the Qualification threshold?
At 800 mg total daily dose
Reported peak | Threshold | Above QF threshold?
 | 0.15% | 
Reported peak | Equivalent in mg | Above QF threshold?

## Slide 34: Example 1
A peak is observed at 0.086%.
Is this above the Qualification threshold?
At 800 mg total daily dose
Reported peak | Threshold | Above QF threshold?
0.09% | 0.15% | 
Reported peak | Equivalent in mg | Above QF threshold?
0.09% |  | 

## Slide 35: Example 1
A peak is observed at 0.086%.
Is this above the Qualification threshold?
At 800 mg total daily dose
Reported peak | Threshold | Above QF threshold?
0.09% | 0.15% | No
Reported peak | Equivalent in mg | Above QF threshold?
0.09% |  | 

## Slide 36: Example 1
A peak is observed at 0.086%.
Is this above the Qualification threshold?
At 800 mg total daily dose
Reported peak | Threshold | Above QF threshold?
0.09% | 0.15% | No
Reported peak | Equivalent in mg | Above QF threshold?
0.09% | 0.72 mg | 

## Slide 37: Example 1
A peak is observed at 0.086%.
Is this above the Qualification threshold?
At 800 mg total daily dose
Reported peak | Threshold | Above QF threshold?
0.09% | 0.15% | No
Reported peak | Equivalent in mg | Above QF threshold?
0.09% | 0.72 mg | No

## Slide 38: Example 2
A peak is observed at 0.086%.
Is this above the Qualification threshold?
At 1150 mg total daily dose
Reported peak | Threshold | Above QF threshold?
0.09% | 0.15% | 
Reported peak | Equivalent in mg | Above QF threshold?
0.09% |  | 

## Slide 39: Example 2
A peak is observed at 0.086%.
Is this above the Qualification threshold?
At 1150 mg total daily dose
Reported peak | Threshold | Above QF threshold?
0.09% | 0.15% | No
Reported peak | Equivalent in mg | Above QF threshold?
0.09% |  | 

## Slide 40: Example 2
A peak is observed at 0.086%.
Is this above the Qualification threshold?
At 1150 mg total daily dose
Reported peak | Threshold | Above QF threshold?
0.09% | 0.15% | No
Reported peak | Equivalent in mg | Above QF threshold?
0.09% | 1.035 mg | 

## Slide 41: Example 2
A peak is observed at 0.086%.
Is this above the Qualification threshold?
At 1150 mg total daily dose
Reported peak | Threshold | Above QF threshold?
0.09% | 0.15% | No
Reported peak | Equivalent in mg | Above QF threshold?
0.09% | ~1.0 mg | 

## Slide 42: Example 2
A peak is observed at 0.086%.
Is this above the Qualification threshold?
At 1150 mg total daily dose
Reported peak | Threshold | Above QF threshold?
0.09% | 0.15% | No
Reported peak | Equivalent in mg | Above QF threshold?
0.09% | ~1.0 mg | No

## Slide 43: Example 3
A peak is observed at 0.086%.
Is this above the Qualification threshold?
At 1800 mg total daily dose
Reported peak | Threshold | Above QF threshold?
0.09% | 0.15% | No
Reported peak | Equivalent in mg | Above QF threshold?
0.09% |  | 

## Slide 44: Example 3
A peak is observed at 0.086%.
Is this above the Qualification threshold?
At 1800 mg total daily dose
Reported peak | Threshold | Above QF threshold?
0.09% | 0.15% | No
Reported peak | Equivalent in mg | Above QF threshold?
0.09% | 1.62 mg | 

## Slide 45: Example 3
A peak is observed at 0.086%.
Is this above the Qualification threshold?
At 1800 mg total daily dose
Reported peak | Threshold | Above QF threshold?
0.09% | 0.10% | No
Reported peak | Equivalent in mg | Above QF threshold?
0.09% | 1.6 mg | Yes

## Slide 46: Example 4
A peak is observed at 0.086%.
Is this above the Qualification threshold?
At 2500 mg total daily dose
Reported peak | Threshold | Above QF threshold?
0.09% |  | 
Reported peak | Equivalent in mg | Above QF threshold?
0.09% |  | 

## Slide 47: Example 4
A peak is observed at 0.086%.
Is this above the Qualification threshold?
At 2500 mg total daily dose
Reported peak | Threshold | Above QF threshold?
0.09% | 0.05% | Yes
Reported peak | Equivalent in mg | Above QF threshold?
0.09% |  | 

## Slide 48: Relative response factors
API
Imp A
Imp B
Which impurity peak is bigger?
UV Abs

## Slide 49: Relative response factors
API
Imp A
Imp B
Which impurity is present in the greater amount?
UV Abs

## Slide 50: Relative response factors
API
Imp A
Imp B
Which impurity is present in the greater amount?
It is impossible to tell without further information.
UV Abs

## Slide 51: Relative response factors
The size of a peak in a chromatogram is determined by the amount of impurity present, but also how well it responds to the detector.
In HPLC-UV techniques the response is due to the inherent UV absorbance of the impurity at the detected wavelength.
Some impurities will not be detected at all!
        RRF = Response of Imp/Response of API, but always check the formula just in case the ratio is described differently.

## Slide 52: Response factors
At the time of initial development and investigation it is assumed the response factor = 1.
For reporting thresholds it is assumed the response factor = 1.
When impurities are identified their response factor must be considered.
The RRF for all identified impurities should be established.

## Slide 53: Relative response factors
When an RRF of between 0.8 to 1.2 is it not mandatory to apply the correction.
The use of a RRF could shift an observed impurity from one threshold to another.
This is often of benefit to the applicant. If the response of an impurity is greater than the equivalent amount of API (RRF>1) it could mean a peak no longer exceeds the Qualification threshold.

## Slide 54: Conclusion
The applicant should discuss the possible generation of related substances in 3.2.S.3.2
They must undertake a rigorous testing investigation, including use of appropriate test methods.
Monographs are an excellent source of information on possible related substances and degradation impurities but are not complete.
When applying thresholds consider TDI and RRF of the impurity

## Slide 55: Further information
Please feel free to ask me any questions now or later.
http://www.who.int/prequal/info_applicants/API_info_applicants.htm
Or email me at:
Fakea@who.int
Thank you